## Slide 1: Chapter 5: Path Control Implementation
CCNP ROUTE: Implementing IP Routing
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 5 Objectives
Using Cisco Express Forwarding Switching
Understanding Path Control
Implementing Path Control Using Policy-Based Routing
Implementing Path Control Using Cisco IOS IP SLAs
Notes: Chapter 1 Objectives

## Slide 3: Using Cisco Express Forwarding Switching

## Slide 4: Using Cisco Express Forwarding Switching
Describe the different switching mechanisms that a Cisco router uses
Describe how Cisco Express Forwarding (CEF) works
Describe how to verify that CEF is working
Describe how to verify the content of the CEF tables
Describe how to enable and disable CEF by interface and globally

## Slide 5: Control and Data Plane
A Layer 3 device employs a distributed architecture in which the control plane and data plane are relatively independent.
For example, the exchange of routing protocol information is performed in the control plane by the route processor, whereas data packets are forwarded in the data plane by an interface micro-coded processor.

## Slide 6: Control and Data Plane
The main functions of the control layer between the routing protocol and the firmware data plane microcode include the following:
  Managing the internal data and control circuits for the packet-forwarding and control functions.
  Extracting the other routing and packet-forwarding-related control information from Layer 2 and Layer 3 bridging and routing protocols and the configuration data, and then conveying the information to the interface module for control of the data plane.
  Collecting the data plane information, such as traffic statistics, from the interface module to the route processor.
  Handling certain data packets that are sent from the Ethernet interface modules to the route processor.

## Slide 7: Cisco Switching Mechanisms
Process switching
Fast switching
Cisco Express Forwarding

## Slide 8: Process switching

## Slide 9: Process switching
This switching method is the slowest of the three methods.
Every packet is examined by the CPU in the control plane and all forwarding decisions are made in software.
When a packet arrives on the ingress interface, it is forwarded to the control plane where the CPU matches the destination address with an entry in its routing table.
It then determines the exit interface and forwards the packet.
The router does this for every packet, even if the destination is the same for a stream of packets.
Process switching is the most CPU-intensive method that is available in Cisco routers. It greatly degrades performance and is generally used only as a last resort or during troubleshooting.

## Slide 10: Fast switching

## Slide 11: Fast switching
This switching method is faster than process switching.
With fast switching, the initial packet of a traffic flow is process switched.
This means that it is examined by the CPU and the forwarding decision is made in software.
However, the forwarding decision is also stored in the data plane hardware fast-switching cache.
When subsequent frames in the flow arrive, the destination is found in the hardware fast-switching cache and the frames are then forwarded without interrupting the CPU.

## Slide 12: Cisco Express Forwarding

## Slide 13: Cisco Express Forwarding
This switching method is the fastest switching mode and is less CPU-intensive than fast switching and process switching.
The control plane CPU of a CEF-enabled router creates two hardware-based tables called the Forwarding Information Base (FIB) table and an adjacency table using Layer 3 and 2 tables including the routing and Address Resolution Protocol (ARP) tables.
When a network has converged, the FIB and adjacency tables contain all the information a router would have to consider when forwarding a packet.
These two tables are then used to make hardware-based forwarding decisions for all frames in a data flow, even the first frame.
The FIB contains precomputed reverse lookups and next-hop information for routes, including the interface and Layer 2 information.
Notes: While CEF is the fastest switching mode, some limitations apply. Some features are not compatible with CEF. In some rare instances, too, the functions of CEF can actually degrade performance.
Note Packets that cannot be CEF switched, such as packets destined to the router itself, are “punted.” This means that the packet will be fast switched or process switched.

## Slide 14: Process and Fast Switching
Notes: When the first packet of a packet flow arrives for destination 10.0.0.0/8, the router initially looks for the destination in its fast-switching cache. Because the destination is not in the fast-switching cache, the router must perform process switching.
Therefore, a full routing table lookup is performed. The process performs a recursive lookup to find the outgoing interface.
Process switching might trigger an ARP request or find the Layer 2 address in the ARP cache. For example, the MAC address of 172.16.1.2 was found in the ARP cache, as shown in Figure 5-6

## Slide 15: Process and Fast Switching
Specifically, an entry is created in the fast-switching cache to ensure that the subsequent packets for the same destination prefix will be fast switched.
All subsequent packets for the same destination are fast switched:
  The switching occurs in the interrupt code. (The packet is processed immediately.)
  Fast destination lookup is performed (no recursion).
  The encapsulation uses a pregenerated Layer 2 header that contains the destination IP Address and Layer 2 source MAC address. (No ARP request or ARP cache lookup is necessary.)

## Slide 16: Cisco Express Forwarding

## Slide 17: Cisco Express Forwarding
CEF separates the control plane software from the data plane hardware, thereby achieving higher data throughput.
The control plane is responsible for building the FIB table and adjacency tables in software.
The data plane is responsible for forwarding IP unicast traffic using hardware.

## Slide 18: CEF FIB Table
The FIB is derived from the IP routing table and is arranged for maximum lookup throughput.
CEF IP destination prefixes are stored from the most-specific to the least specific entry.
The FIB lookup is based on the Layer 3 destination address prefix (longest match), so it matches the structure of CEF entries. When the CEF FIB table is full, a wildcard entry redirects frames to the Layer 3 engine.
The FIB table is updated after each network change, but only once, and contains all known routes; there is no need to build a route cache by central-processing initial packets from each data flow.
Each change in the IP routing table triggers a similar change in the FIB table because it contains all next-hop addresses that are associated with all destination networks.

## Slide 19: CEF Adjancency Table
CEF also caches Layer 2 next-hop addresses and frame header rewrite information for all FIB entries in the adjacency table.
The adjacency table is derived from the ARP table, and it contains Layer 2 header rewrite (MAC) information for each next hop that is contained in the FIB.
Each time that an adjacency entry is created (such as through ARP), a link-layer header for that adjacent node is precomputed and is stored in the adjacency table.
CEF uses a specific process to build forwarding tables in the hardware and then uses the information from those tables to forward packets at line speed.

## Slide 20: CEF Exceptions
Not all packets can be CEF switched and processed in the hardware. When traffic cannot be processed in the hardware, it must be received by software processing of the Layer 3 engine.
Some examples of IP exception packets are packets that have the following characteristics:
They use IP header options.
They have an expiring IP Time To Live (TTL) counter.
They are forwarded to a tunnel interface.
They arrive with unsupported encapsulation types.
They are routed to an interface with unsupported encapsulation types.
They exceed the maximum transmission unit (MTU) of an output interface and mustbe fragmented.

## Slide 21: Enable and Disable CEF by Interface

## Slide 22: Enable and Disable CEF Globally

## Slide 23
Understanding Path Control

## Slide 24: Understanding Path Control
Identify the need for path control
Describe how to use policy-based routing (PBR) to control path selection
Describe how to use IP service-level agreement (IP SLA) to control path selection

## Slide 25: The Need for Path Control
Path control tools can be used to change the default destination forwarding and optimize the path of the packets for some specific application.
Other examples of path control include switching traffic to the backup link if there is a primary link failure, or forwarding some traffic to the backup link if the primary link is congested.
Path control mechanisms can improve performance in such a situation.
Similarly, load balancing can divide traffic among parallel paths.
It is important to provide predictable and deterministic control over traffic patterns.
Unfortunately, there is not a “one-command” solution to implement path control.
Notes: Networks are designed to use redundancy to provide high availability. However, having redundancy does not guarantee resistance to failure.
The use of multiple routing protocols and redundant connectivity options can result in inefficient paths for forwarding packets to their destinations.
Each routing protocol has a different administrative distance, metric, and convergence time. Suboptimal routing often occurs after redistribution because redistribution resets the administrative distance and metric.
Convergence time is also important. First, protocols converge in different ways from each other and for different network designs. Second, slow convergence can result in an application sending traffic timeouts before a backup path is found to a destination. Path control is required to avoid performance issues and to optimize paths.

## Slide 26: The Need for Path Control
You can use all of these tools as part of an integrated strategy to implement path control.

## Slide 27: Implementing Path Control Using Policy-Based Routing
PBR enables the administrator to define a routing policy other than basic destination-based routing using the routing table.
With PBR, route maps can be used to match source and destination addresses, protocol types, and end-user applications.
When a match occurs, a set command can be used to define items, such as the interface or next-hop address to which the packet should be sent.

## Slide 28: PBR Features
Source-based transit-provider selection
  PBR policies can be implemented by ISPs and other organizations to route traffic that originates from different sets of users through different Internet connections across the policy routers.
QoS
  PBR policies can be implemented to provide quality of service (QoS) to differentiated traffic by setting the type of service (ToS) values in the IP packet headers in routers at the periphery of the network and then leveraging queuing mechanisms to prioritize traffic in the network’s core or backbone.
Cost savings
  PBR policies can be implemented to direct the bulk traffic associated with a specific activity to use a higher-bandwidth, high-cost link for a short time and to continue basic connectivity over a lower-bandwidth, low-cost link for interactive traffic.
Load sharing
  PBR policies can be implemented based on the traffic characteristics to distribute traffic among multiple paths.
Notes: PBR is a powerful and flexible tool that offers significant benefits in terms of implementing user-defined policies to control traffic in the internetwork.
PBR adds flexibility in a difficult-to-manage environment by providing the ability to route traffic that is based on network needs.
It also provides solutions in cases where legal, contractual, or political constraints dictate that traffic be routed through specific paths.

## Slide 29: Steps for Configuring PBR
Enable PBR by configuring a route map using the route-map global configuration command.
Implement the traffic-matching configuration, specifying which traffic will be manipulated. This is done using the match commands within the route map.
Define the action for the matched traffic. This is done using the set commands within the route map.
Optionally, fast-switched PBR or CEF-switched PBR can be enabled.
Apply the route map to incoming traffic or to traffic locally generated on the router using the ip policy route-map interface configuration command.
Notes: Fast-switched PBR must be enabled manually. CEF-switched PBR is automatically enabled when CEF switching is enabled (which it is by default in recent IOS versions) and PBR is enabled.
6. Verify PBR configuration with basic connectivity and path verification commands, as well as policy routing show commands.

## Slide 30: Configuring PBR – Route-Map
If the statement is marked as permit , such as in route-map MY-MAP permit 10 , packets that meet all the match criteria are policy-based routed.
If the statement is marked as deny , such as in route-map MY-MAP deny 10 , a packet meeting the match criteria is not policy-based routed. Instead, it is sent through the normal forwarding channels and destination-based routing is performed.
If no match is found in the route map, the packet is not dropped. It is forwarded through the normal routing channel, which means that destination-based routing is performed.

## Slide 31: PBR match Commands

## Slide 32: PBR set Commands

## Slide 33: Configuring PBR Example
Verify normal traffic paths as selected by the traditional destination-based routing
Configure PBR to alter the traffic flow for one client station
Verify both the PBR configuration and the new traffic path

## Slide 34: Verify Normal Traffic Paths

## Slide 35: Configure PBR to Alter the Traffic Flow from the Notebook

## Slide 36: Verify the PBR Configuration and Traffic Path

## Slide 37: Implementing Path Control Using Cisco IOS IP SLAs
PBR is a static path control mechanism. It cannot respond dynamically to changes in network health.

## Slide 38: IP SLA Features
Cisco IOS IP SLAs perform network performance measurement within Cisco devices.
The IP SLAs use active traffic monitoring (generation of traffic in a continuous, reliable, and predictable manner) for measuring network performance.
Cisco IOS IP SLAs actively send simulated data across the network to measure performance between multiple network locations or across multiple network paths.
The information collected includes data about response time, one-way latency, jitter, packet loss, voice-quality scoring, network resource availability, application performance, and server response time.
In its simplest form, Cisco IOS IP SLAs verify whether a network element, such as an IP address on a router interface or an open TCP port on an IP host, is active and responsive.

## Slide 39: Cisco IOS IP SLA Sources and Targets
Notes: However, the IP SLA responder can be configured to capture specific data that can be retrieved by the source using the CLI or through an SNMP tool that supports the operation of IP SLAs. The IP SLA measurement accuracy is improved when the target is an IP SLA responder.

## Slide 40: Steps for Configuring IP SLAs
Step 1. Define one or more IP SLA operations (or probes).
Step 2. Define one or more tracking objects to track the state of IOS IP SLA operations.
Step 3. Define the action associated with the tracking object.

## Slide 41: Step 1. Configuring Cisco IOS IP SLA Operations
Use the ip sla operation-number global configuration command to begin configuring a Cisco IOS IP SLA operation and to enter IP SLA configuration mode. The operationnumber is the identification number of the IP SLA operation to be configured.

## Slide 42: IP SLA icmp-echo
The complete command syntax is icmp-echo { destination-ip-address | destinationhostname} [ source-ip { ip - address | hostname } | source-interface interface-name ].

## Slide 43: IP SLA ICMP Echo Configuration Mode Commands

## Slide 44: Schedule the IP SLA Operation
Once a Cisco IP SLA operation is configured, it needs to be scheduled using the ip sla schedule global configuration command.
ip sla schedule operation-number [ life { forever | seconds }] [ start-time { hh:mm [ :ss ] [ month day | day month ] | pending | now | after hh:mm:ss }] [ ageout seconds ] [ recurring ]

## Slide 45: Step 2: Configuring Cisco IOS IP SLA Tracking Objects
Use the track object-number ip sla operation-number { state | reachability } global configuration command to track the state of an IOS IP SLA operation, and enter track configuration mode.

## Slide 46: delay Command Parameters
Once in IP SLA track configuration mode, use the optional delay { up seconds [ down seconds ] | [ up seconds ] down seconds } track configuration command to specify a period of time to delay communicating state changes of a tracked object.

## Slide 47: Step 3: Defining an Action Associated with a Tracking Object
Many types of actions can be associated with a tracked object.
A simple path control action is to use the ip route prefix mask { ip-address | interface-type interface-number [ ip-address ]} [ track number ] global configuration command.
The command can be used with the track keyword to establish a static route that tracks an object.
Notes: To display configuration values including all defaults for all Cisco IOS IP SLA operations, or for a specified operation, use the show ip sla configuration [ operation ] command. The operation parameter is the number of the IP SLA operation for which the details will be displayed.

## Slide 48: Configuring IP SLA Example
The static route to ISP1a (ISP-1), which has been assigned an administrative distance of 2
The static route to ISP2a (ISP-2), which has been assigned an administrative distance of 3

## Slide 49: In the example, you will
Configure an IP SLA operation with the ISP 1 DNS server
Define a tracking object assign an action
Configure an IP SLA operation with the ISP 2 DNS server
Define a tracking object assign an action

## Slide 50: Configure IP SLA and Track Object for ISP 1

## Slide 51: Configure IP SLA and Track Object for ISP 2

## Slide 52: Configuring PBR and IP SLA Example
In this scenario, traffic paths for the clients at first branch office (router BR1) will be optimized using PBR and IP SLA. EIGRP is already configured between HQ and BR1, and all traffic flows over the Ethernet WAN link because it has the lowest EIGRP metric route.

## Slide 53: In the example, you will
The new network policy for BR1 dictates that
  Web traffic to the HQ site should be redirected over the serial link.
  All other traffic from Notebook should go via BR2 but only if BR2 is reachable.
In the example, you will
  Redirect web traffic from clients on the BR1 router going to the HQ router over the serial link using PBR
  Ensure that BR2 is reachable by using an IP SLA ICMP echo test to its WAN interface
  Redirect all other traffic from Notebook to router BR2 if BR2 is reachable

## Slide 54: Redirecting Web Traffic from BR1 to HQ Using PBR

## Slide 55: Ensuring That BR2 Is Reachable Using IP SLA

## Slide 56: Redirect Traffic from Notebook to BR2 If Reachable

## Slide 57: Verify Route Maps

## Slide 58: Verify That the Route Map Is Applied

## Slide 59: Verify IP SLA Operations

## Slide 60: Verify Tracking Objects

## Slide 61: Chapter 5 Summary
Packet-switching mechanisms on a Cisco IOS platform, including process switching, fast switching, and CEF switching.
Overview of path control tools, including PBR and Cisco IOS IP SLAs.
Using PBR to control path selection, providing benefits including source-based transit provider selection, QoS, cost savings, and load sharing. PBR is applied to incoming packets; enabling PBR causes the router to evaluate all packets incoming on the interface using a route map configured for that purpose.
Configuring and verifying PBR, including the following steps:
  Choose the path control tool to use; for PBR, route-map commands are used
  Implement the traffic-matching configuration, specifying which traffic will be manipulated; match commands are used within route maps
  Define the action for the matched traffic, using set commands within route maps
  Apply the route map to incoming traffic or to traffic locally generated on the router
  Verify path control results, using show commands

## Slide 62: Chapter 5 Summary
Cisco IOS IP SLAs, which use active traffic monitoring, generating traffic in a continuous, reliable, and predictable manner, to measure network performance. IOS IP SLAs can be used in conjunction with other tools, including the following:
  Object tracking, to track the reachability of specified objects
  Cisco IOS IP SLAs probes, to send different types of probes toward the desired objects
  Static routes with tracking options, as a simpler alternative to PBR
  Route maps with PBR, to associate the results of the tracking to the routing process
Cisco IOS IP SLA terminology, including the following:
  All the Cisco IOS IP SLA measurement probe operations are configured on the IP SLA source, either by the CLI or through an SNMP tool that supports IP SLA operation. The source sends probe packets to the target.
  There are two types of IP SLA operations: those in which the target device is running the IP SLA responder component, and those in which the target device is not running the IP SLA responder component (such as a web server or IP host).
  An IP SLA operation is a measurement that includes protocol, frequency, traps, and thresholds.
Configuring and verifying IOS IP SLAs.

## Slide 63: Chapter 5 Labs
CCNPv7 ROUTE Lab5.1 Path Control Using PBR
CCNPv7 ROUTE Lab 5.2 IP SLA Tracking and Path Control

## Slide 65: Acknowledgment
Some of images and texts are from Implementing Cisco IP Routing (ROUTE) Foundation Learning Guide by Diane Teare, Bob Vachon and Rick Graziani (1587204568)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva