## Slide 1: Chapter 6: Enterprise Internet Connectivity
CCNP ROUTE: Implementing IP Routing
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 6 Objectives
Planning Enterprise Internet Connectivity
Establishing Single-Homed IPv4 Internet Connectivity
Establishing Single-Homed IPv6 IPv6 Internet Connectivity
Improving Internet Connectivity Resilience
Notes: Chapter 1 Objectives

## Slide 3: Planning Enterprise Internet Connectivity

## Slide 4: Planning Enterprise Internet Connectivity
Identify the Internet connectivity needs of organizations
Identify the different types of ISP connectivity
Describe public IP address assignments and the need for provider-independent IP addressing
Describe autonomous system numbers

## Slide 5: Connecting Enterprise Networks to an ISP
Enterprise Connectivity Requirements
Outbound
  In the rare case that only one-way connectivity outbound from clients to the Internet is required, private IPv4 addresses with Network Address Translation (NAT) are used for IPv4 connections, allowing clients on a private network to communicate with servers on the public Internet.
Inbound
  Two-way connectivity is needed, so that clients external to the enterprise network can access resources in the enterprise network. In this case, both public and private IPv4 address space is needed, as are routing and security considerations.

## Slide 6: Redundancy for Enterprise Network to ISP connectivity
Edge device redundancy
  Deploying redundant edge devices, such as routers, protects your network against device failure. If one router fails, Internet connectivity can still be established through the redundant router.
Link redundancy
  Using redundant links protects your network against link failure between your router and the ISP router.
ISP redundancy
  If you are hosting important servers in your network or accessing mission-critical servers in the Internet, it is best to have two redundant ISPs. If a failure occurs in one ISP network, traffic can be automatically rerouted through the second ISP.

## Slide 7: ISP Redundancy
Single-homed
  With a connection to a single ISP when no link redundancy is used, the customer is single-homed. Single-homed ISP connectivity is used in cases when a loss in Internet connectivity is not problematic to a customer.
Dual-homed
  With a connection to a single ISP, redundancy can be achieved if two links toward the same ISP are used effectively.
  There are two options for dual homing: Both links can be connected to one customer router, or to enhance the resiliency further, the two links can terminate at separate routers in the customer’s network.
  In either case, routing must be properly configured to allow both links to be used.

## Slide 8: ISP Redundancy
Multihomed
  With connections to multiple ISPs, redundancy is built in to the design.
  Connections from different ISPs can terminate on the same router, or on different routers to further enhance the resiliency.
  The customer is responsible for announcing its own IP address space to upstream ISPs, but should avoid forwarding any routing information between ISPs (otherwise the customer becomes a transit provider between the two ISPs). The routing used must be capable of reacting to dynamic changes. Multihoming also allows load balancing of traffic between ISPs.
Dual multihomed
  To enhance the resiliency further with connections to multiple ISPs, a customer can have two links toward each ISP.

## Slide 9: ISP Redundancy

## Slide 10: Public IP Address Assignment
The Internet Assigned Numbers Authority (IANA):
Coordinate the global pool of IPv4 and IPv6 addresses, and provide them to RIRs
Coordinate the global pool of autonomous system numbers and provide them to RIRs
Manage the Domain Name Service (DNS) root zone
Manage the IP numbering systems (in conjunction with standards bodies)

## Slide 11: Regional Internet Registries
African Network Information Centre (AfriNIC)
  Responsible for the continent of Africa
Asia Pacific Network Information Centre (APNIC)
  Administers the numbers for the Asia Pacific region
American Registry for Internet Numbers (ARIN)
  Has jurisdiction over assigning numbers for Canada, the United States, and several islands in the Caribbean Sea and North Atlantic Ocean
Latin American and Caribbean IP Address Regional Registry (LACNIC)
  Responsible for allocation in Latin America and portions of the Caribbean
Reséaux IP Européens Network Coordination Centre (RIPE NCC)
  Administers the numbers for Europe, the Middle East, and Central Asia

## Slide 12: Public IP Address Space
Provider Aggregatable Address Space
  A PA block of IP addresses is used in simple topologies, where no redundancy is needed.
  PA address space is assigned by the ISP to its customer, from its address space.
  If the customer changes its ISP, the new ISP will give the customer a new PA address space, and all devices with public IP addresses will have to be renumbered; the old address space cannot be transferred to the new.

## Slide 13: Public IP Address Space
Provider-Independent Address Space
  For a multihomed connection, a PI address space is required because the enterprise network needs to be independent of the ISP’s address space.
  The PI address space must be acquired from an RIR; it is assigned directly to an organization by the RIR, and is not related to any ISP.
  This address space can be routed through other service providers, resulting in more flexibility when planning connections to ISPs and when migrating between service providers.
  After successfully processing an address space request, the RIR assigns the PI address space and a public autonomous system number (ASN) (described in the next section) that uniquely defines the enterprise’s network and its address spaces.
  This ASN is not related to any ISP.
  The enterprise then configures their Internet gateway routers to advertise the newly assigned IP address space to neighboring ISPs; the Border Gateway Protocol (BGP) is typically used for this task.

## Slide 14: Autonomous System Numbers
The ASN is a very important parameter required when configuring BGP.

## Slide 15: Reserved ASN
The IANA defines the following two ASN ranges to be used for private purposes, much like the private IPv4 addresses:
  64,512 through 65,534
  4,200,000,000 through 4,294,967,294 (64,086.59904 through 65,535.65534)
The IANA also defines the following two ranges for use in documentation and in sample code:
  64,496 through 64,511
  65,536 through 65,551

## Slide 16
Establishing Single-Homed IPv4 Internet Connectivity

## Slide 17: Establishing Single-Homed IPv4 Internet Connectivity
Describe how to configure your router with both a provider-assigned static IPv4 address and a provider-assigned DHCP address
Understand DHCP operation and describe how to use a router as a DHCP server and relay agent
Identify the various types of NAT
Describe the NAT virtual interface (NVI) feature, configuration, and verification

## Slide 18: Configuring a Provider-Assigned IPv4 Address
Step 1. Assign the static IPv4 address on the router’s Internet-facing interface.
Step 2. Configure a default route that will forward all traffic intended for the Internet to the ISP.

## Slide 19: DHCP Operation
Four other DHCP messages are possible:
DHCPDECLINE: A message sent from a client to a server indicating that the address is already in use
DHCPNAK: A message sent from a server indicating that it is refusing a client’s request for configuration
DHCPRELEASE: A message sent from a client indicating to a server that it is giving up a lease
DHCPINFORM: A message sent from a client indicating that it already has an IPv4 address, but is requesting other configuration parameters from the DHCP server, such as a DNS address

## Slide 20: Obtaining a Provider-Assigned IPv4 Address with DHCP
When dynamic assignment is used by the ISP, no manual address assignment is needed; instead, DHCP client functionality needs to be enabled on the router interface. Other configuration information can also be obtained through DHCP, such as the default gateway address.
Notes: The default route is installed with an administrative distance (AD) of 254, making it a floating static route; the high AD prevents the injected route from being used if other manually configured or dynamically learned default routes exist. You can disable this functionality by issuing the no ip dhcp client request router interface configuration command.

## Slide 21: Configuring a Router as a DHCP Server and DHCP Relay Agent

## Slide 22: NAT
NAT is usually implemented on border devices such as firewalls or routers, which allows devices within an organization to have private addresses.
NAT translates private addresses to public addresses and vice versa, keeping a mapping between the two for return traffic.
NAT can be configured to translate all private addresses to only one public address or to pick from a pool of public addresses.
RFC 1918, Address Allocation for Private Internets , has set aside the following IPv4 address space for private use:
  Class A network: 10.0.0.0 to 10.255.255.255
  Class B network: 172.16.0.0 to 172.31.255.255
  Class C network: 192.168.0.0 to 192.168.255.255

## Slide 23: NAT
NAT uses the terms inside and outside . Inside means internal to your network, and outside means external to your network. NAT includes the following four types of addresses:
Inside local address
  The IPv4 address assigned to a device on the internal network.
Inside global address
  The IPv4 address of an internal device as it appears to the external network. This is the address to which the inside local address is translated.
Outside local address
  The IPv4 address of an external device as it appears to the internal network. If outside addresses are being translated, this is the address to which the outside global address is translated.
Outside global address
  The IPv4 address assigned to a device on the external network.

## Slide 24: Types of NAT
Static NAT
  Static NAT is one-to-one translation. Static NAT is particularly useful when a device must be accessible from outside the network
Dynamic NAT
  Dynamic NAT is many-to-many translation, using a pool of addresses. When an inside device accesses an outside network, it is assigned an available IPv4 address from the pool on a first-come, first-serve basis. When using dynamic NAT, you need to ensure that there are enough addresses available in the pool to satisfy the total number of user sessions.
Port Address Translation (PAT)
  PAT is many-to-one translation; for example, it maps multiple inside local IPv4 addresses to a single inside global IPv4 address by tracking port numbers. PAT is also known as NAT overloading .

## Slide 25: Configuring Static NAT
Using the ip nat inside source static local-ip global-ip global configuration command.

## Slide 26: Configuring Static NAT - Example

## Slide 27: Configuring Dynamic NAT
ip nat inside source list { access-list-number | access-list-name } pool name

## Slide 28: Configuring Dynamic NAT - Example

## Slide 29: Configuring PAT
ip nat inside source list { access-list-number | access-list-name } { interface type number } [ overload]

## Slide 30: Configuring PAT - Example

## Slide 31: Limitations of NAT
End-to-end visibility issues: Many applications depend on end-to-end functionality, with unmodified packets being forwarded from source to destination. By changing end-to-end addresses, NAT effectively blocks such applications.
Tunneling becomes more complex: Using NAT can complicate tunneling protocols, such as IPsec, because NAT modifies the values in the headers and thus interferes with the integrity checks done by IPsec and other tunneling protocols.

## Slide 32: Limitations of NAT
In certain topologies, standard NAT may not work correctly
  R1 router is configured to perform PAT for the LAN clients and static NAT for the web server.
  When a client on the Internet wants to access the web server, it gets the server’s public IP address from the DNS. The router statically translates the server’s public IP address to its inside local address, and forwards packets to the server.
  When a client on the LAN tries to access the server, it similarly gets the same public IP address for the server from DNS, and tries to access the server. However, attempts to connect to the server will fail because of how NAT operates.
  When packets go from inside to outside, they are first routed and then translated; the packets from the LAN client are routed to the outside interface and the LAN client’s address is translated by PAT. When packets travel from outside to inside, they are translated and routed. In this case however, the packets from the LAN client do not come into the router’s outside interface; therefore, they are never translated so they are never routed back to the interface where the server is located.
  The result is that the LAN client cannot connect to the web server.

## Slide 33: NAT Virtual Interface
As of Cisco IOS Software Release 12.3(14)T Cisco introduced a new feature, NAT virtual interface (NVI), which removes the requirement to configure an interface as inside or outside.
The NVI order of operations is also slightly different than NAT.
Recall that classic NAT first performs routing and then translation when going from an inside interface to an outside interface, and vice versa when the traffic flow is reversed.
NVI, however, performs routing, translation, and routing again; NVI performs the routing operation twice, before and after translation, before forwarding the packet to an exit interface.
The whole process is symmetrical, no matter which way the traffic is flowing.
Because of the added routing step, packets can flow, in classic NAT terms, from an inside to an inside interface; as described in the previous section, this scenario fails if classic NAT is used.

## Slide 34: Configuring NAT Virtual Interface
Notes: The first step is to identify the addresses to be translated dynamically using an access list. Because only the 192.168.10.0/24 segment should be translated dynamically, a standard access list using the access-list 10 permit 192.168.10.0 0.0.0.255 global configuration command is created.
Notice that there are no inside or outside keywords used in these commands. Because NVI does not require that you define inside or outside interfaces, those keywords are also not used in the translation commands.

## Slide 35: Configuring NAT Virtual Interface

## Slide 36: NVI Interface
When a packet enters the NAT router on any NAT-enabled interface, it is matched against the NAT translation table.
If there is a match, the packet is routed to the NVI0 interface, where translation takes place. After the translation process, the packet is routed again and forwarded to the appropriate interface.
The NVI0 interface is assigned an IPv4 address, which is needed for Cisco IOS internal operation. The assigned IPv4 address has no influence on NAT behavior; it is copied from the first physical interface or from the first interface on which NAT is enabled.

## Slide 37: show ip nat nvi translations
Notes: Notice that the output of the command differs slightly from legacy NAT command output. Because NVI no longer uses inside and outside, the terms inside global , inside local , outside local , and outside global are no longer used in the translations table. Instead, the terms source global , source local , destin local , and destin global are used, respectively.
The definition of the terms, however, remains the same.

## Slide 38: show ip nat nvi statistics

## Slide 39
Establishing Single-Homed IPv6 Internet Connectivity

## Slide 40: Establishing Single-Homed IPv6 Internet Connectivity
Describe the various ways that your router can obtain an IPv6 address
Understand DHCP for IPv6 (DHCPv6) operation and describe the use of a router as a DHCPv6 server and relay agent
Describe the use of NAT for IPv6
Identify how to configure IPv6 ACLs
Describe the need to secure IPv6 Internet connectivity

## Slide 41: Obtaining a Provider-Assigned IPv6 Address
The IPv6 address assignment methods are as follows:
Manual assignment
Stateless address autoconfiguration (SLAAC)
Stateless DHCPv6
Stateful DHCPv6
DHCPv6 prefix delegation (DHCPv6-PD)

## Slide 42: Manual Assignment
As with IPv4, an IPv6 address can be statically assigned by a network administrator.
This assignment method can be error-prone and introduces significant administrative overhead, especially because of the 128-bit length of IPv6 addresses.

## Slide 43: Configuring Basic IPv6 Internet Connectivity

## Slide 44: Stateless Address Autoconfiguration
SLAAC provides the capability for a device to obtain IPv6 addressing information without any intervention from the network administrator.
This is achieved with the help of RAs, which are sent by routers on the local link.
RA messages include one or more prefixes, prefix lifetime information, flag information, and default router lifetime information.
The source IPv6 link-local address of the RA message is used by the host as its IPv6 default router address.
IPv6 hosts listen for these RAs and use the advertised prefix, which must be 64 bits long.
The host generates the remaining 64 host bits either by using the IEEE EUI-64 format or by creating a random sequence of bits.
If the generated IPv6 address is unique, it can be applied to the interface.
This process introduces plug-and-play functionality to the network, which significantly reduces administrative overhead; however, it provides no way of tracking address assignment.

## Slide 45: IEEE EUI-64
The MAC address is split into two 24-bit parts.
0xFFFE is inserted between the two parts, resulting in a 64-bit value.
The seventh bit of the first octet is inverted. (In a MAC address, this bit indicates the scope and has a value of 0 for global scope and 1 for local scope; it will be 0 for globally unique MAC addresses. In the EUI-64 format used for IPv6 interface IDs, the meaning of this bit is opposite, so the bit is inverted.)

## Slide 46: Enabling SLAAC
Use the ipv6 address autoconfig [ default ] interface configuration command to enable automatic configuration of IPv6 addresses using SLAAC.
The optional default keyword causes a default route to be installed using that default router.
You can specify the default keyword on only one interface.
Note that the commands configured on a router determine when it generates router solicitation (RS) and RA messages:
  Routers configured with the ipv6 unicast-routing command generate RA messages. They do not generate RS messages.
  Routers configured with the ipv6 address autoconfig command, and not configured with the ipv6 unicast-routing command, generate RS messages only. They do not generate RA messages.

## Slide 47: DHCPv6 Operation
In the IPv6 world, there are two types of DHCPv6:
Stateless: Used to supply additional parameters to clients that already have an IPv6 address
Stateful: Similar to DHCP for IPv4 (DHCPv4)

## Slide 48: Stateless DCHPv6
Stateless DHCPv6 works in combination with SLAAC.
An IPv6 host gets its addressing and default router information using SLAAC, from information contained within an RA.
However, the IPv6 host also queries a DHCPv6 server for other information it needs, such as the DNS or NTP server addresses.
The query for other configurations is triggered by the other configuration flag bit set in the RA.
In this case, the DHCPv6 server does not assign IPv6 addresses, and therefore does not need to maintain any dynamic state information for the clients; therefore, it is called stateless .
Notes: Note that because of the use of SLAAC, however, the issue of address tracking is still not resolved.
The RA link-local address is still used as the default router address.

## Slide 49: Configuring Stateless DCHPv6

## Slide 50: Stateful DHCPv6
When stateful DHCPv6 is implemented, RAs use the managed address configuration flag bit to tell IPv6 hosts to get their addressing and additional information only from the DHCPv6 server.
This flag tells the hosts to disregard the prefixes in the RA and instead query the DHCPv6 server for addressing and other information.
The DHCPv6 server then allocates addresses to the host and tracks the allocated address.
Note that the default router address is still received from the RA link-local address.

## Slide 51: Configuring Stateful DHCPv6
Notes: DHCPv6 Prefix Delegation
DHCPv6-PD is an extension to DHCPv6. It is used by an ISP to automate the process of assigning prefixes to a customer for use within the customer’s network. The prefix delegation occurs between a provider-edge (PE) device and customer premise equipment (CPE) using the DHCPv6-PD option. Once the ISP has delegated prefixes to a customer, the customer may further subnet and assign prefixes to the links in their network.

## Slide 52: DHCPv6 Operation
The client sends a SOLICIT message to find a DHCPv6 server and request assignment of addresses and other configuration information.
This message is sent to the all-DHCP-agents multicast address (FF02::1:2) with link-local scope
Any DHCPv6 servers that can meet the client’s requirement respond to the client with an ADVERTISE message.
The client chooses one of the servers and sends a REQUEST message to it, asking it to confirm the addresses and other information that were advertised.
The server responds with a REPLY message that contains the confirmed addresses and configuration information.
Like with DHCPv4, a DHCPv6 client renews its lease after a period of time by sending a RENEW message.
By default, the four-message exchange is used; when the rapid-commit option is enabled by both the client and server, the two-message exchange is used (SOLICIT-REPLY).
Notes: A DHCPv6 client builds a list of potential servers by sending a SOLICIT message and collecting ADVERTISE message replies from servers. These messages are ranked based on preference value; servers may add an explicit preference option to their ADVERTISE messages. If the client needs to acquire prefixes from a server, only servers that have advertised prefixes are considered.
In addition to the four-way exchange, DHCPv6 can also use a shortened two-way exchange, with only SOLICIT and REPLY messages. By default, the four-message exchange is used; when the rapid-commit option is enabled by both the client and server, the two-message exchange is used.

## Slide 53: NAT for IPv6
In IPv4, NAT is typically used to translate private addresses to public addresses when communicating on the Internet. In IPv6, we do not have to worry about private-to-public address translation, but some forms of NAT are still used.
NAT64
NAT64 performs both address and IP header translation. An example use of NAT64 is to provide IPv4 Internet connectivity to IPv6 devices, during the transition to a full IPv6 Internet.
NPTv6
NPTv6 is described in RFC 6296, IPv6-to-IPv6 Network Prefix Translation . (Note that at the time of this writing this RFC has an “experimental,” not “standard,” status.)
NPTv6 is a one-to-one stateless translation; one IPv6 address in an inside network, such as an organization’s LAN, is translated to one IPv6 address in an outside network, the IPv6 Internet.

## Slide 54: IPv6 ACLs
One change from IPv4 is that IPv6 ACLs are always named and extended.
For IPv6, there are three implicit rules at the end of each ACL, as follows:
  permit icmp any any nd-na
  permit icmp any any nd-ns
  deny ipv6 any any
If you want to log all packets that are denied, simply add a deny ipv6 any any log command to your ACL.
However, this explicit deny command would override all three implicit rules, you would need to explicitly configure the two permit nd statements, followed by the explicit deny statement.
Notes: The first of these rules permits all ND neighbor advertisement (NA) messages.
The second permits all ND neighbor solicitation (NS) messages. The last denies all other IPv6
packets.
If you want to log all packets that are denied, you may be tempted to do as you would in IPv4 and simply add a deny ipv6 any any log command to your ACL.
However, this explicit deny command would override all three implicit rules, not just the last one, and would result in the neighbor discovery traffic being blocked. You would need to instead explicitly configure the two permit nd statements, followed by the explicit deny statement.

## Slide 55: Configuring IPv6 ACLs

## Slide 56: Verifying IPv6 ACLs

## Slide 57
Improving Internet Connectivity Resilience

## Slide 58: Improving Internet Connectivity Resilience
Describe the disadvantages of single-homed Internet connectivity
Describe dual-homed Internet connectivity
Describe multihomed Internet connectivity

## Slide 59: Drawbacks of a Single-Homed Internet Connectivity

## Slide 60: Dual-Homed Internet Connectivity

## Slide 61: Configuring Best Path for Dual-Homed Internet Connectivity
In dual-homed networks, one link is usually used as a primary link. In case of primary link failure, the second (backup) link is used for traffic forwarding.
Either static routing toward the ISP or BGP with the ISP are commonly used to route outbound traffic.
Internet routing information must also be available to the organization’s internal routing protocol. In simple networks, static routes with different ADs (called floating static routes) can be used.
Alternatively, you can redistribute a default route or a subset of Internet routes into your internal routing protocol.
First-hop redundancy protocols (FHRPs) can also be used to properly route packets to the appropriate Internet gateway.

## Slide 62: Dual-Homed EIGRP and Static Example

## Slide 63: Multihomed Internet Connectivity
The multihomed Internet design offers the highest level of redundancy. It resolves all single points of failure issues and provides a reliable link to the Internet.
Two routers are commonly used as Internet gateways, and each router is connected to a different ISP using one or more physical links.

## Slide 64: Multihomed Internet Connectivity
Establishing a multihomed environment involves meeting some requirements:
  You must have PI (Provider Independent) address space and your own autonomous system number.
  You must establish connectivity with two independent ISPs.

## Slide 65: Options for Routes That ISPs in a Multihomed Design Can Send
The ISPs can send the following to your network:
  The ISPs can send only a default route.
  The ISPs can send a partial routing table and a default route.
  The ISPs could also send you a full routing table.
Notes: The ISPs can send the following to your network:
  The ISPs can send only a default route. Your border Internet routers then typically select one default route as the best, and send all traffic to that ISP.
  The ISPs can send a partial routing table (of a subset of routes originated near the ISP) and a default route. This option allows you to use all the links to the ISPs. In this case, the border Internet routers calculate the best paths to each destination and use this for optimal routing. In Figure 6-19 , for example, traffic to customers connected to ISP1 will usually be routed to ISP1, and traffic to customers connected to ISP2 will be redirected to ISP2.
  The ISPs could also send you a full routing table. In this case, your border Internet gateways calculate optimal paths for all Internet traffic.

## Slide 66: Chapter 6 Summary
Internet connectivity requirements: outbound only, or also inbound.
Internet connectivity redundancy options: edge device, link, and ISP.
The four connection redundancy types:
  Single-homed: One connection to one ISP
  Dual-homed: Two connections to one ISP
  Multihomed: One connection to each of multiple (usually two) ISPs
  Dual multihomed: Two connections to each of two ISPs
Public IP address assignment: The IANA assigns to RIRs; RIRs assign to ISPs and organizations.

## Slide 67: Chapter 6 Summary
IP addresses, which can be PI or PA.
Routing protocols that are either IGPs (and operate within an autonomous system) or EGPs (and operate between autonomous systems). BGP is the protocol used between autonomous systems on the Internet.
The range of private autonomous system numbers: 64,512 to 65,534 and 4,200,000,000 through 4,294,967,294 (64,086.59904 through 65,535.65534).
Provider-assigned IPv4 addresses, which can be configured statically or via DHCP.
DHCPv4 operation, including the DHCPDISCOVER, DHCPOFFER, DHCPREQUEST, and DHCPACK messages.
The use of NAT for IPv4, typically to translate private addresses to public addresses.

## Slide 68: Chapter 6 Summary
The four types of NAT addresses:
  Inside local address: The IPv4 address assigned to a device on the internal network.
  Inside global address: The IPv4 address of an internal device as it appears to the external network. This is the address to which the inside local address is translated.
  Outside local address: The IPv4 address of an external device as it appears to the internal network. If outside addresses are being translated, this is the address to which the outside global address is translated.
  Outside global address: The IPv4 address assigned to a device on the external network.
The three types of NAT: static (one-to-one), dynamic (many-to-many), and PAT (many-to-one).
The order of operations for NAT: It first performs routing and then translation when going from an inside interface to an outside interface, and vice versa when the traffic flow is reversed.

## Slide 69: Chapter 6 Summary
NAT issues, including when an inside device tries to communicate with a device on another inside interface.
NVI, which removes the requirement to configure an interface as inside or outside. NVI also operates differently; it performs routing, translation, and routing again. The whole process is symmetrical, no matter which way the traffic is flowing.
Configuring a Cisco router to be a DHCP server and a DHCP relay agent, for both IPv4 and IPv6.
IPv6 addresses, which can be configured with the following methods:
  Manual Assignment
  SLAAC
  Stateless DHCPv6
  Stateful DHCPv6
  DHCPv6-PD

## Slide 70: Chapter 6 Summary
DHCPv6 operation, including the SOLICIT, ADVERTISE, REQUEST, and REPLY messages.
Two types of NAT for IPv6: NAT64 and NPTv6.
IPv6 ACLs, which include three implicit rules at the end of each ACL, as follows:
  permit icmp any any nd-na
  permit icmp any any nd-ns
  deny ipv6 any any
Applying an IPv6 ACL to an interface, using the ipv6 traffic-filter ACL-name { in|out } interface configuration command. Notice the traffic-filter keyword is used rather than the access-group keyword that is used in IPv4 ACLs.
The need to secure devices connected to the IPv6 Internet.
The drawbacks of single-homed Internet connectivity because of the single points of failure: link failure, ISP failure, or router failure.

## Slide 71: Chapter 6 Summary
Using a dual-homed design to improve redundancy: two (or more) connections, using one or more Internet routers, to the same ISP. The ISP may also have multiple routers to connect to specific customers. Static routes or BGP are used. One link can be primary, or traffic can be load balanced over both links.
Using a multihomed design to further improve redundancy; two routers are used as Internet gateways, and each router is connected to a different ISP using one or more physical links.
The options for what ISPs can send to your network in a multihomed design:
  Only a default route
  A partial routing table (of a subset of routes originated near the ISP) and a default route
  A full routing table
How receiving full routing tables consume a lot of router resources.

## Slide 72: Chapter 6 Labs
CCNPv7 ROUTE Lab6.1 NAT

## Slide 74: Acknowledgment
Some of images and texts are from Implementing Cisco IP Routing (ROUTE) Foundation Learning Guide by Diane Teare, Bob Vachon and Rick Graziani (1587204568)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva