## Slide 1: Chapter 7: BGP Implementation
CCNP ROUTE: Implementing IP Routing
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 7 Objectives
BGP Terminology, Concepts, and Operation
Implementing Basic BGP
BGP Attributes and the Path-Selection Process
Controlling BGP Routing Updates
Implementing BGP for IPv6 Internet Connectivity
Notes: Chapter 1 Objectives

## Slide 3: BGP Terminology, Concepts, and Operation

## Slide 4: BGP Path Vector Characteristics
The path vector information includes a list of the full path of BGP autonomous system numbers (hop by hop) necessary to reach a destination network; this is the AS-path attribute.
The autonomous system path information is used to construct a loop-free graph, since router running BGP does not accept a routing update that already includes its autonomous system number in the path list.
Notes: Other attributes include the IP address to get to the next autonomous system (the next-hop attribute) and how the networks at the end of the path were introduced into BGP (the origin code attribute).

## Slide 5: BGP Terminology, Concepts, and Operation
Using BGP between autonomous systems
Comparing BGP with other scalable routing protocols
BGP path vector characteristics
BGP characteristics
BGP tables
BGP message types
When to use BGP
When not to use BGP

## Slide 6: BGP Use Between Autonomous Systems
The main goal of BGP is to provide an interdomain routing system that guarantees the loop-free exchange of routing information between autonomous systems. BGP routers exchange information about paths to destination networks.
Notes: BGP’s interdomain routing enables connectivity between autonomous systems and is usually based on a set of policies, not just the technical characteristics of the underlying infrastructure.

## Slide 7: BGP Path Vector Characteristics
BGP allows routing-policy decisions to be applied to the path of BGP autonomous system numbers so that routing behavior can be enforced at the autonomous system level and to determine how data will flow through the autonomous system.
The policies are based on the attributes carried in the routing information and configured on the routers.
BGP specifies that a BGP router can advertise to its peers (neighbors) in neighboring autonomous systems only those routes that it uses.
This rule reflects the hop-by-hop routing paradigm generally used throughout the current Internet.
Some policies cannot be supported by the hop-by-hop routing paradigm.
For example, BGP does not allow one autonomous system to send traffic to a neighboring autonomous system, intending that the traffic take a different route from that taken by traffic originating in that neighboring autonomous system.
Notes: In other words, you cannot influence how a neighboring autonomous system will route your traffic, but you can influence how your traffic gets to a neighboring autonomous system. However, BGP can support any policy conforming to the hop-by-hop routing paradigm.

## Slide 8: BGP Path Vector Characteristics
64520 64600 64700
64520 64600 64540 64550 64700
64520 64540 64600 64700
64520 64540 64550 64700
Autonomous system 64512 does not see all these possibilities.
Autonomous system 64520 advertises to autonomous system 64512 only its best path (in this case, 64520 64600 64700), the same way that IGPs announce only their best least-metric routes. This path is the only path through autonomous system 64520 that autonomous system 64512sees.

## Slide 9: BGP Supports the Internet’s Hop-by-Hop Routing Paradigm
To reach the networks in autonomous system 64700, autonomous system 64512 can choose to use the path through autonomous system 64520 or it can choose to go through the path that autonomous system 64530 is advertising.
Autonomous system 64512 selects the best path to take based on its own BGP routing policies.

## Slide 10: BGP Characteristics
BGP is sometimes categorized as an advanced distance vector protocol, but it is actually a path vector protocol.
BGP uses the Transmission Control Protocol (TCP) as its transport protocol, which provides connection-oriented reliable delivery.
In this way, BGP assumes that its communication is reliable and, therefore, BGP does not have to implement any retransmission or error-recovery mechanisms, like EIGRP does.
BGP information is carried inside TCP segments using protocol 179

## Slide 11: BGP Packet

## Slide 12: BGP Characteristics
Two routers speaking BGP (called BGP speakers ) establish a TCP connection with one another and exchange messages to open and confirm the connection parameters.
These two routers are called BGP peer routers or BGP neighbors
After the TCP connection is made, the routers exchange their full BGP tables
However, because the connection is reliable, BGP routers need to send only changes (incremental updates) after that.
Periodic routing updates are not required on a reliable link, so triggered updates are used.
BGP sends keepalive messages, similar to the hello messages sent by OSPF and EIGRP.
Notes: BGP is the only IP routing protocol to use TCP as its transport layer.
OSPF and EIGRP reside directly above the IP layer, and RIP uses the User Datagram Protocol (UDP) for its transport layer. OSPF and EIGRP have their own internal functions to ensure that update packets are explicitly acknowledged.
These protocols use a one-for-one window so that if either OSPF or EIGRP has multiple packets to send, the next packet cannot be sent until an acknowledgment from the first update packet is received. This process can be very inefficient and cause latency issues if thousands of update packets must be exchanged over relatively slow serial links.
However, OSPF and EIGRP rarely have thousands of update packets to send. For example, EIGRP can hold more than 100 networks in one EIGRP update packet, so 100 EIGRP update packets can hold up to 10,000 networks.
Most organizations do not have 10,000 subnets.
BGP, however, has many more networks on the Internet to advertise (as of 2014 there were 500,000, and growing); it uses TCP to handle the acknowledgment function. TCP uses a dynamic window, which allows for up to 65,576 bytes to be outstanding before it stops and waits for an acknowledgment. For example, if 1000-byte packets are being sent and the maximum window size is being used, BGP would have to stop and wait for an acknowledgment only if 65 packets had not been acknowledged.
TCP is designed to use a sliding window, where the receiver sends an acknowledgment before the number of octets specified by the window have been received (such as the halfway point of the sending window). This method allows any TCP application, such as BGP, to continue streaming packets without having to stop and wait, as OSPF or EIGRP would require.

## Slide 13: BGP Tables
BGP keeps a neighbor table containing a list of neighbors with which it has a BGP connection.
BGP also keeps its own table for storing BGP information received from and sent to other routers.

## Slide 14: BGP Table
It is important to remember that this BGP table is separate from the IP routing table in the router.
The router offers the best routes from the BGP table to the IP routing table and can be configured to share information between the two tables (by redistribution).

## Slide 15: BGP Routing Process
For BGP to establish an adjacency, you must configure it explicitly for each neighbor.
BGP forms a TCP relationship with each of the configured neighbors and keeps track of the state of these relationships by periodically sending a BGP/TCP keepalive message.
After establishing an adjacency, the neighbors exchange their best BGP routes.
Each router collects these routes from each neighbor with which it successfully established an adjacency and places them in its BGP table; all routes that have been learned from each neighbor are placed in the BGP table.
Each path learned is associated with BGP attributes. The single best route for each network is selected from the BGP table using these attributes in the BGP route-selection process and then offered to the IP routing table.

## Slide 16: BGP Routing Process
Each router compares the offered BGP routes to any other possible paths to those networks in its IP routing table, and the best route, based on administrative distance, is installed in the IP routing table.
External BGP (eBGP) routes (BGP routes learned from an external autonomous system) have a default administrative distance of 20.
Internal BGP (iBGP) routes (BGP routes learned from within the autonomous system) have a default administrative distance of 200.
A router may have a best BGP route to a destination, but that route might not be installed in the IP routing table because it has a higher administrative distance than another route.
That best BGP route will still be propagated to other BGP routers, though.

## Slide 17: BGP Message Types
BGP defines the following message types:
Open
Keepalive
Update
Notification
Notes: Note Keepalive messages have a length of 19 bytes. Other messages may be between 19 and 4096 bytes long.

## Slide 18: Open and Keepalive Messages
After a TCP connection is established, the first message sent by each side is an open message.
If the open message is acceptable, a keepalive message confirming the open message is sent back by the side that received the open message.
When the open is confirmed, the BGP connection is established, and update, keepalive, and notification messages can be exchanged.
BGP peers initially exchange their full BGP routing tables.
From then on, incremental updates are sent as the table changes.
Keepalive packets are sent to ensure that the connection is alive between the BGP peers, and notification packets are sent in response to errors or special conditions.

## Slide 19: Open Message
An open message includes the following information:
Version
  8-bit field. BGP implementations today use the current version, BGP-4.
My autonomous system
  16-bit field indicates the sender’s autonomous system number. The peer router verifies this information; if it is not the autonomous system number expected, then the BGP session is torn down.
Hold time
  16-bit field indicates the maximum number of seconds that can elapse between the successive keepalive or update messages from the sender
BGP router identifier (router ID)
  This 32-bit field indicates the sender’s BGP identifier. The BGP router ID is an IP address assigned to that router and is determined at startup.
Optional parameters
  A length field indicates the total length of the optional parameters field in octets. These parameters are Type, Length, and Value(TLV) encoded.
  An example of an optional parameter is session authentication.
Notes: Hold time
  16-bit field indicates the maximum number of seconds that can elapse between the successive keepalive or update messages from the sender. Upon receipt of an open message, the router calculates the value of the hold timer to use with this neighbor by using the smaller of its configured hold time (which has a default of 180 seconds) and the hold time received in the open message.
BGP router identifier (router ID)
  This 32-bit field indicates the sender’s BGP identifier. The BGP router ID is an IP address assigned to that router and is determined at startup. The BGP router ID is chosen the same way the OSPF router ID is chosen: It is the highest active IP address on the router, unless a loopback interface with an IP address exists, in which case it is the highest such loopback IP address. Alternatively, the router ID can be statically configured, overriding the automatic selection.

## Slide 20: Update Messages
An update message has information on one path only; multiple paths require multiple messages. All the attributes in the update message refer to that path, and the networks are those that can be reached through that path.
An update message might include the following fields:
Withdrawn routes
  A list of IP address prefixes for routes that are being withdrawn from service, if any.
Path attributes
  The AS-path, origin, local preference, and so forth. Each path attribute includes the attribute type, attribute length, and attribute value (TLV).
Network layer reachability information (NLRI)
  A list of networks (IP address prefixes and their prefix lengths) that can be reached by this path.

## Slide 21: Notification Messages
A BGP router sends a notification message when it detects an error condition. The BGP router closes the BGP connection immediately after sending the notification message.
Notification messages include an error code, an error subcode, and data related to the error.

## Slide 22: BGP Neighbor States
BGP is a state machine that takes a router through the following states with its neighbors:
Idle
Connect
Active
Open sent
Open confirm
Established
Only when the connection is in the established state are update, keepalive, and notification messages exchanged.
Notes: Neighbor states are discussed in more detail in the “Understanding and Troubleshooting BGP Neighbor States” section, later in this chapter.

## Slide 23: When to Use BGP
BGP use in an autonomous system is most appropriate when the effects of BGP are well understood and at least one of the following conditions exists:
The autonomous system allows packets to transit through it to reach other autonomous systems (for example, it is a service provider).
The autonomous system has multiple connections to other autonomous systems.
Routing policy and route selection for traffic entering and leaving the autonomous system must be manipulated.

## Slide 24: When Not to Use BGP
Do not use BGP if one or more of the following conditions exist:
A single connection to the Internet or another autonomous system.
Lack of memory or processor power on edge routers to handle constant BGP updates.
You have a limited understanding of route filtering and the BGP path-selection process.
If the routing policy that will be implemented in an autonomous system is consistent with the policy implemented in the ISP autonomous system.

## Slide 25
Implementing Basic BGP

## Slide 26: Implementing Basic BGP
BGP neighbor relationships
Basic BGP configuration requirements
Entering BGP configuration mode
Defining BGP neighbors and activating BGP sessions
Basic BGP configuration and verification

## Slide 27: BGP Neighbor Relationships
No single router can handle communications with the tens of thousands of the routers that run BGP and are connected to the Internet, representing more than 48,000 autonomous systems.
A BGP router forms a direct neighbor relationship with a limited number of other BGP routers.
Through these BGP neighbors, a BGP router learns of the paths through the Internet to reach any advertised network.
Recall that any router that runs BGP is called a BGP speaker.
A BGP peer, also known as a BGP neighbor, is a BGP speaker that is configured to form a neighbor relationship with another BGP speaker for the purpose of directly exchanging BGP routing information with one another.

## Slide 28: BGP Neighbor Relationships
BGP peers can be either internal or external to the autonomous system.

## Slide 29: External BGP Neighbors

## Slide 30: External BGP Neighbors
There are several requirements for an eBGP neighbor relationship (also called an eBGP neighborship):
Different autonomous system number
  eBGP neighbors must reside in different autonomous systems to be able to form an eBGP relationship.
Define neighbors
  A TCP session must be established before starting BGP routing update exchanges.
Reachability
  The IP addresses used in the neighbor command must be reachable; eBGP neighbors are usually directly connected.

## Slide 31: Internal BGP Neighbors

## Slide 32: Internal BGP Neighbors
There are several requirements for an iBGP neighbor relationship (also known as an iBGP neighborship):
Same autonomous system number
  iBGP neighbors must reside in the same autonomous system to be able to form an iBGP relationship.
Define neighbors
  A TCP session must be established between neighbors before they start exchanging BGP routing updates.
Reachability
  iBGP neighbors must be reachable. An IGP typically runs inside the autonomous system, and provides this reachability.

## Slide 33: iBGP in a Transit Autonomous System

## Slide 34: iBGP in a Transit Autonomous System
A transit autonomous system, such as autonomous system 65102 , is an autonomous system that routes traffic from one external autonomous system to another external autonomous system.
Transit autonomous systems are typically ISPs. All routers in a transit autonomous system must have complete knowledge of external routes.
One way to achieve this goal is to redistribute BGP routes into an IGP at the edge routers; however, this approach has problems.
Because the current Internet routing table is very large, redistributing all the BGP routes into an IGP is not a scalable way for the interior routers within an autonomous system to learn about the external networks.
Another method that you can use is to run iBGP on all routers within the autonomous system.

## Slide 35: iBGP in a Nontransit Autonomous System
A nontransit autonomous system, such as an organization that is multihoming with two ISPs, does not pass routes between the ISPs.
To make proper routing decisions, however, the BGP routers within the autonomous system still require knowledge of all BGP routes passed to the autonomous system.
BGP does not work in the same manner as IGPs.
Because the designers of BGP could not guarantee that an autonomous system would run BGP on all routers, a method had to be developed to ensure that iBGP speakers could pass updates to one another while ensuring that no routing loops would exist.

## Slide 36: TCP and Full Mesh
TCP sessions cannot be multicast or broadcast because TCP has to ensure the delivery of packets to each recipient. Because TCP cannot use broadcasting or multicasting, BGP cannot use it either.
To avoid routing loops within an autonomous system, BGP specifies that routes learned through iBGP are never propagated to other iBGP peers; this is sometimes referred to as the BGP split-horizon rule.
Thus, each iBGP router needs to send routes to all the other iBGP neighbors in the same autonomous system.
Because they cannot use broadcast or multicast, an iBGP neighbor relationship must be configured between each pair of routers.
Recall that the neighbor command enables BGP updates between BGP speakers.
By default, each BGP speaker is assumed to have a neighbor statement for all other iBGP speakers in the autonomous system; this is known as full-mesh iBGP .
When a change is received from an external autonomous system, the receiving BGP router is responsible for informing all of its iBGP neighbors of the change.
iBGP neighbors that receive this update do not send it to any other iBGP neighbor because they assume that the sending iBGP neighbor is fully meshed with all other iBGP speakers and has sent each iBGP neighbor the update.
Notes: If the sending iBGP neighbor is not fully meshed with each iBGP router, the routers that are not peering with this router will have different IP routing tables than the routers that are peering with it. The inconsistent routing tables can cause routing loops or routing black holes, because the default assumption by all routers running BGP within an autonomous system is that each BGP router exchanges iBGP information directly with all other BGP routers in the autonomous system.

## Slide 37: BGP Partial-Mesh and Full-Mesh Examples

## Slide 38: Basic BGP Configuration Requirements
The next step is to gather the parameters needed to provide the BGP configuration details. For basic BGP, these details include the following:
The autonomous system numbers (of your own network and of all remote autonomous systems)
The IP addresses of all the neighbors (peers) involved
The networks that are to be advertised into BGP
Basic BGP configuration requires the following main steps:
Step 1. Define the BGP process.
Step 2. Establish the neighbor relationships.
Step 3. Advertise the networks into BGP.

## Slide 39: Entering BGP Configuration Mode
Use the router bgp autonomous-system global configuration command to enter BGP configuration mode and identify the local autonomous system in which this router belongs.
The BGP process needs to be informed of its autonomous system so that when BGP neighbors are configured it can determine whether they are iBGP or eBGP neighbors.
Only one instance of BGP can be configured on a router at a time. For example, if you configure your router in autonomous system 65000 and then try to configure the router bgp 65100 command, the router informs you that you are currently configured for autonomous system 65000.
Notes: The router bgp command alone does not activate BGP on a router. You must enter at least one subcommand under the router bgp command to activate the BGP process on the router.

## Slide 40: Defining BGP Neighbors and Activating BGP Sessions
Use the neighbor ip-address remote-as autonomous-system router configuration command to activate a BGP session for external and internal neighbors and to identify a peer router with which the local router will establish a session.

## Slide 41: BGP Configuration Example
R1
R2
R3

## Slide 42: Basic BGP Configuration and Verification

## Slide 43: Configuring and Verifying an eBGP Session

## Slide 44: Verifying an eBGP Session
The first part of this command output describes the local router:
BGP router identifier: The IP address that all other BGP speakers recognize as representing this router
Local AS number: The local router’s autonomous system number
The next part of this command output describes the BGP table:
BGP table version: This is the version number of the local BGP table; it increases when the BGP table changes.
Main routing table version: This is the last version of BGP database that was injected into the main routing table.

## Slide 45: Verifying an eBGP Session
The rest of this command output describes the current neighbor status, one for each configured neighbor:
Neighbor: The IP address, used in the neighbor statement
Version (V): The version of BGP this router is running with the listed neighbor.
AS: The listed neighbor’s autonomous system number.
Messages received (MsgRcvd): The number of BGP messages received from this neighbor.
Messages sent (MsgSent): The number of BGP messages sent to this neighbor.
TblVer: The last version of the BGP table that was sent to this neighbor.
In queue (InQ): The number of messages from this neighbor that are waiting to be processed.
Out queue (OutQ): The number of messages queued and waiting to be sent to this neighbor. TCP flow control prevents this router from overwhelming a neighbor with a large update.
Up/down: The length of time this neighbor has been in the current BGP state (established, active, or idle).
State: The current state of the BGP session : active, idle, open sent, open confirm, or idle (admin).
Prefix received (PfxRcd): When the session is in the established state, this value represents the number of BGP network entries received from this neighbor.
Notes: The admin state indicates that the neighbor is administratively shut down; this state is created by using the neighbor ip-address shutdown router configuration command. The active state means that the router is attempting to create a TCP connection to this neighbor. (Neighbor states are discussed in more detail in the “Understanding and Troubleshooting BGP Neighbor States” section, later in this chapter.) Note that if the session is in the established state, a state is not displayed. Instead, a number representing the PfxRcd is displayed, as described next.

## Slide 46: Verifying an eBGP Session
The show ip bgp neighbors command supplies additional information, such as the negotiated capabilities, supported address families, and others.

## Slide 47: show ip bgp neighbors Command Options

## Slide 48: Configuring and Verifying an iBGP Session

## Slide 49: Configuring and Verifying an iBGP Session

## Slide 50: Advertising Networks in BGP
Use the network network-number [ mask network-mask ] router configuration command to inject routes that are present in the IPv4 routing table into the BGP table so that they can be advertised in BGP.

## Slide 51: Advertising Networks in BGP
It is important to note that the BGP network command determines which networks this router advertises.
Unlike for IGPs, the network command does not start BGP on specific interfaces.
Rather, it indicates to BGP which networks it should originate from this router.
The list of network commands must include all networks in your autonomous system that you want to advertise, not just those locally connected to your router.
The mask parameter indicates that BGP-4 allows classless prefixes; it can advertise subnets and supernets.
Notice the difference between the neighbor command and the network command: The neighbor command tells BGP where to advertise; the network command tells BGP what to advertise.
If the mask parameter is not specified, this command announces only the classful network number; at least one subnet of the specified major network must be present in the IP routing table to allow BGP to start announcing the classful network as a BGP route.

## Slide 52: Advertising Networks in BGP
If the mask network-mask is specified, an exact match to the network (both address and mask) must exist in the routing table for the network to be advertised.
Before BGP announces a route, it checks to see whether it can reach it.
For example, if you want to advertise the 192.168.0.0/24 route, and by mistake you configure network 192.168.0.0 mask 255.255.0.0 instead of network 192.168.0.0 mask 255.255.255.0 , BGP looks for 192.168.0.0/16 in the routing table. In this case, it would find 192.168.0.0/24 but will not find 192.168.0.0/16. Because the routing table does not contain a specific match to the network, BGP does not announce the 192.168.0.0/24 network to any neighbors.
If you want to advertise the CIDR block 192.168.0.0/16, you might try configuring network 192.168.0.0 mask 255.255.0.0. Again, BGP looks for 192.168.0.0/16 in the routing table, and if it never finds 192.168.0.0/16, BGP does not announce the 192.168.0.0/16 network to any neighbors. In this case, you can configure a static route to the CIDR block toward the null interface, with the ip route 192.168.0.0 255.255.0.0 null0 command, so that BGP can find an exact match in the routing table.
After finding an exact match in the routing table, BGP announces the 192.168.0.0/16 network to its neighbors.

## Slide 53: Advertising Networks in BGP - Example

## Slide 54: Examining the BGP Table
The status codes are shown at the beginning of each line of output, and the origin codes are shown at the end of each line.
A row with an asterisk (*) in the first column means that the next-hop address is valid.
A greater-than sign ( > ) in the second column indicates the best path for a route selected by BGP.
This route is offered to the IP routing table.
Notes: An s indicates that the specified routes are suppressed (usually because routes have been summarized and only the summarized route is being sent).
A d , for dampening, indicates that the route is being dampened (penalized) for going up and down too often. Although the route might be up right now, it is not advertised until the penalty has expired.
An h , for history, indicates that the route is unavailable and is probably down. Historic information about the route exists, but a best route does not exist.
An r , for Routing Information Base (RIB) failure, indicates that the route was not installed in the RIB; the RIB is another name for the IP routing table. The reason that the route is not installed can be displayed using the show ip bgp rib-failure command, as described in the next section.
An S , for stale, indicates that the route is stale. (This is used in a nonstop forwardingaware router.)

## Slide 55: Examining the BGP Table
The third column is either blank or has an i in it. If it is blank, BGP learned that route from an external peer. If it has an i , an iBGP neighbor advertised this route to this router.
The fourth column lists the networks that the router learned.
If this column contains 0.0.0.0, this router originated the route.

## Slide 56: Examining the BGP Table
The next three columns list three BGP path attributes associated with the path: metric, which is also called the multi-exit discriminator (MED); local preference; and weight.
The column with the Path header may contain a sequence of autonomous systems in the path.
From left to right, the first autonomous system listed is the adjacent autonomous system from which this network was learned.

## Slide 57: Examining the BGP Table
If the last column has an i in it, the original router probably used a network command to introduce this network into BGP.
The character e signifies that the original router learned this network from EGP, which is the historic predecessor to BGP.
A question mark ( ? ) signifies that the original BGP process cannot absolutely verify this network’s availability because it is redistributed from an IGP into the BGP process.

## Slide 58: Examining the BGP Table

## Slide 59: Next-Hop-Self Feature

## Slide 60: Next-Hop-Self Feature

## Slide 61: Next-Hop-Self Feature
Notice, though, that the entry is not designated as a best route; the > character is missing.
This is because R3 does not have a route to the next-hop address (209.165.202.129), and therefore the route is not installed in the routing table.

## Slide 62: Configuring Next-Hop

## Slide 63: Understanding and Troubleshooting BGP Neighbor States
After the TCP handshake is complete, the BGP application tries to set up a session with the neighbor. BGP is a state machine that takes a router through the following states with its neighbors:
Idle
  The router is searching the routing table to see whether a route exists to reach the neighbor.
Connect
  The router found a route to the neighbor and has completed the threeway TCP handshake.
Open sent
  An open message was sent, with the parameters for the BGP session.
Open confirm
  The router received agreement on the parameters for establishing a session.
  Alternatively, the router goes into the active state if there is no response to the open message.
Established
  Peering is established and routing begins.
Notes: After you enter the neighbor remote-as command, BGP starts in the idle state, and the BGP process checks that it has a route to the IP address listed.
BGP should be in the idle state for only a few seconds. However, if BGP does not find a route to the neighboring IP address, it stays in the idle state.
If it finds a route, it goes to the connect state when the TCP handshaking synchronize acknowledge (SYN ACK) packet returns (when the TCP three-way handshake is complete). After the TCP connection is set up, the BGP process creates a BGP open message and sends it to the neighbor. After BGP dispatches this open message, the BGP peering session changes to the open sent state. If there is no response for 5 seconds, the state changes to the active state. If a response does come back in a timely manner, BGP goes to the open confirm state and starts scanning (evaluating) the routing table for the paths to send to the neighbor. When these paths have been found, BGP then goes to the established state and begins routing between the neighbors.

## Slide 64: idle state
After you enter the neighbor remote-as command, BGP starts in the idle state, and the BGP process checks that it has a route to the IP address listed.
BGP should be in the idle state for only a few seconds.
However, if BGP does not find a route to the neighboring IP address, it stays in the idle state.

## Slide 65: connect state
If it finds a route, it goes to the connect state when the TCP handshaking synchronize acknowledge (SYN ACK) packet returns (when the TCP three-way handshake is complete). After the TCP connection is set up, the BGP process creates a BGP open message and sends it to the neighbor.

## Slide 66: open sent state
After BGP dispatches this open message, the BGP peering session changes to the open sent state.

## Slide 67: active state
If there is no response for 5 seconds, the state changes to the active state.

## Slide 68: open confirm state
If a response does come back in a timely manner, BGP goes to the open confirm state and starts scanning (evaluating) the routing table for the paths to send to the neighbor.

## Slide 69: established state
When these paths have been found, BGP then goes to the established state and begins routing between the neighbors.
Note:
The BGP state is shown in the last column of the show ip bgp summary command output.

## Slide 70: BGP Session Resilience
In cases where multiple paths exist to reach an iBGP neighboring routers, the routers could peer with each other’s loopback interface address and the BGP session would not be lost because loopback interfaces are always available as long as the router itself does not fail.
This peering arrangement adds resiliency to the iBGP sessions because they are not tied into a physical interface, which might go down for any number of reasons.

## Slide 71: BGP Session Resilience

## Slide 72: Sourcing BGP from Loopback Address
For BGP packets, the source IP address must match the address in the corresponding neighbor statement on the other router. Otherwise, the routers will not be able to establish the BGP session, and the packet will be ignored.
BGP does not accept unsolicited updates; it must be aware of every neighboring router and have a neighbor statement for it.

## Slide 73: Sourcing BGP from Loopback Address

## Slide 74: Sourcing BGP from Loopback Address - eBGP

## Slide 75: eBGP Multihop
To fix this issue, you must also enable multihop eBGP, with the neighbor ip-address ebgp-multihop [ ttl ] router configuration command.
Notes: By default, the TTL is set to 255 with this command

## Slide 76: Resetting BGP Sessions
Hard Reset of BGP Sessions
  Resetting a session is a method of informing the neighbor or neighbors of a policy change. If BGP sessions are reset, all information received on those sessions is invalidated and removed from the BGP table. The remote neighbor detects a BGP session down state and, likewise, invalidates the received routes. After a period of 30 to 60 seconds, the BGP sessions are reestablished automatically, and the BGP table is exchanged again, but through the new filters. However, resetting the BGP session disrupts packet forwarding.
  Use the clear ip bgp * or clear ip bgp { neighbor-address } privileged EXEC command to cause a hard reset of the BGP neighbors involved, where * indicates all sessions and the neighbor-address identifies the address of a specific neighbor for which the BGP sessions will be reset.

## Slide 77: Resetting BGP Sessions
Soft Reset or Route Refresh
  Use the clear ip bgp {* | neighbor-address } out privileged EXEC command to cause BGP to do a soft reset for outbound updates.
  The router on which this command is issued does not reset the BGP session. Instead, the router creates a new update and sends the whole table to the specified neighbors. This update includes withdrawal commands for networks that the neighbor will not see anymore, based on the new outbound policy.
  Outbound BGP soft configuration does not have any memory overhead. This command is highly recommended when you are changing an outbound policy, but does not help if you are changing an inbound policy..

## Slide 78: Monitoring Soft Reconfiguration
When a BGP session is reset using soft reconfiguration, the following commands can be useful for monitoring the BGP routes received, sent, or filtered
  show ip bgp neighbors { address } received-routes: Displays all received routes (both accepted and rejected) from the specified neighbor.
  show ip bgp neighbors { address } routes: Displays all routes that are received and accepted from the specified neighbor. This output is a subset of the output displayed by the received-routes keyword.
  show ip bgp: Displays entries in the BGP table.
  show ip bgp neighbors { address } advertised-routes: Displays all BGP routes that have been advertised to neighbors.

## Slide 79: Monitoring Soft Reconfiguration

## Slide 80
BGP Attributes and the Path-Selection Process

## Slide 81: BGP Path Selection
A router running BGP may receive updates about destinations from multiple neighbors, some in different autonomous systems, and therefore multiple paths might exist to reach a given network.
These are kept in the BGP table.
BGP chooses only a single best path to reach a specific destination.
BGP is not designed to perform load balancing; paths are chosen because of policy, not based on bandwidth.
The BGP selection process eliminates any multiple paths until a single best path is left.
The best BGP path is submitted to the IP routing table manager process and is evaluated against any other routing protocols that can also reach that network.

## Slide 82: BGP Path-Selection Process
Step 1. Prefer the route with the highest weight. (The weight is Cisco proprietary and is local to the router only.)
Step 2. If multiple routes have the same weight, prefer the route with the highest local preference. (The local preference is used within an autonomous system.)
Step 3. If multiple routes have the same local preference, prefer the route that was originated by the local router. (A locally originated route has a next hop of 0.0.0.0 in the BGP table.)
Step 4. If none of the routes were originated by the local router, prefer the route with the shortest AS-path.
Step 5. If the AS-path length is the same, prefer the lowest-origin code (IGP < EGP < incomplete).
Step 6. If all origin codes are the same, prefer the path with the lowest MED. (The MED is exchanged between autonomous systems.)

## Slide 83: BGP Path-Selection Process
Step 7. If the routes have the same MED, prefer external paths (eBGP) over internal paths (iBGP).
Step 8. If only internal paths remain, prefer the path through the closest IGP neighbor. This means that the router prefers the shortest internal path within the autonomous system to reach the destination (the shortest path to the BGP next hop).
Step 9. For eBGP paths, select the oldest route, to minimize the effect of routes going up and down (flapping).
Step 10. Prefer the route with the lowest neighbor BGP router ID value.
Step 11. If the BGP router IDs are the same, prefer the route with the lowest neighbor IP address.

## Slide 84: The Path-Selection Decision Process with a Multihomed Connection
Step 1 looks at weight, which by default is set to 0 for routes that were not originated by this router.
Step 2 compares local preference, which by default is set to 100 for all networks. Both Step 1 and Step 2 have an effect only if the network administrator configures the weight or local preference to a nondefault value.
Step 3 looks at networks that are owned by this autonomous system. If one of the routes is injected into the BGP table by the local router, the local router prefers it to any routes received from other BGP routers.

## Slide 85: The Path-Selection Decision Process with a Multihomed Connection
Step 4 selects the path that has the fewest autonomous systems to cross. This is the most common reason a path is selected in BGP.
Step 5 looks at how a network was introduced into BGP. This introduction is usually either with network commands ( i for an origin code) or through redistribution ( ? for an origin code).
Step 6 looks at MED to judge where the neighbor autonomous system wants this autonomous system to send packets for a given network. The Cisco IOS Software sets the MED to 0 by default. Therefore, MED does not participate in path selection unless the network administrator of the neighbor autonomous system manipulates the paths using MED.

## Slide 86: The Path-Selection Decision Process with a Multihomed Connection
The second most common decision point is Step 7, which states that an externally learned path from an eBGP neighbor is preferred over a path learned from an iBGP neighbor. A router in an autonomous system prefers to use the ISP’s bandwidth to reach a network rather than using internal bandwidth to reach an iBGP neighbor on the other side of its own autonomous system.
If the autonomous system path length is equal and the router in an autonomous system has no eBGP neighbors for that network (only iBGP neighbors), it makes sense to take the quickest path to the nearest exit point. Step 8 looks for the closest iBGP neighbor; the IGP metric determines what closest means.

## Slide 87: The Path-Selection Decision Process with a Multihomed Connection
The oldest path (Step 9) is the next common reason for selecting one path over another. The older neighbor are considered more stable because they have been up longer.
The next most common decision is to take the neighbor with the lowest BGP router ID, which is Step 10.
If the BGP router IDs are the same (for example, if the paths are to the same BGP router), Step 11 states that the route with the lowest neighbor IP address is used.

## Slide 88: BGP Attributes
The following are some terms defining how these attributes are implemented:
An attribute is either well-known or optional, mandatory or discretionary, and transitive or nontransitive. An attribute might also be partial.
Not all combinations of these characteristics are valid; path attributes fall into four separate categories:
  Well-known mandatory
  Well-known discretionary
  Optional transitive
  Optional nontransitive
Only optional transitive attributes might be marked as partial.

## Slide 89: Well-Known Attributes
A well-known attribute is one that all BGP implementations must recognize and propagate to BGP neighbors.
There are two types of well-known attributes:
  Well-known mandatory attribute: A well-known mandatory attribute must appear in all BGP update messages.
  Well-known discretionary attribute: A well-known discretionary attribute does not have to be present in all BGP update messages.
Notes: Note If a well-known attribute is missing from an update message, a notification error is generated. This ensures that all BGP implementations agree on a standard set of attributes.

## Slide 90: Optional Attributes
Attributes that are not well known are called optional.
BGP routers that implement an optional attribute might propagate it to other BGP neighbors, depending on its meaning.
Optional attributes are either transitive or nontransitive, as follows:
  Optional transitive: BGP routers that do not implement an optional transitive attribute should pass it to other BGP routers untouched and mark the attribute as partial.
  Optional nontransitive: BGP routers that do not implement an optional nontransitive attribute must delete the attribute and must not pass it to other BGP routers.

## Slide 91: Defined BGP Attributes
The attributes defined by BGP include the following:
Well-known mandatory attributes
  AS-path
  Next-hop
  Origin
Well-known discretionary attributes
  Local preference
  Atomic aggregate
Optional transitive attributes
  Aggregator
  Community
Optional nontransitive attribute
  MED
In addition, Cisco has defined a weight attribute for BGP. The weight is configured locally on a router and is not propagated to any other BGP routers.

## Slide 92: The AS-Path Attribute
The AS-path attribute is the list of autonomous system numbers that a route has traversed to reach a destination, with the number of the autonomous system that originated the route at the end of the list.
The AS-path attribute is a well-known mandatory attribute

## Slide 93: The Next-Hop Attribute
The BGP next-hop attribute is a well-known mandatory attribute that indicates the next-hop IP address that is to be used to reach a destination.
As discussed earlier, for eBGP the next-hop address is the IP address of the neighbor that sent the update, but for iBGP the next hop advertised by eBGP is carried into iBGP by default.

## Slide 94: The Origin Attribute
The origin is a well-known mandatory attribute that defines the origin of the path information.
The origin attribute can be one of three values:
IGP
  This normally happens when a network command is used to advertise the route via BGP.
  An origin of IGP is indicated with an i in the BGP table.
EGP
  The route is learned via EGP.
  EGP is considered a historic routing protocol and is not supported on the Internet.
Incomplete
  The route’s origin is unknown or is learned via some other means.
  This usually occurs when a route is redistributed into BGP.

## Slide 95: The Local-Preference Attribute
Local preference is a well-known discretionary attribute that indicates to routers in the autonomous system which path is preferred to exit the autonomous system.
A path with a higher local preference is preferred.
The term local refers to inside the autonomous system.
The local preference attribute is sent only to iBGP neighbors; it is not passed to eBGP peers.
The default value for local preference on a Cisco router is 100.

## Slide 96: The Community Attribute
BGP communities allow routers to tag routes with an indicator (the community ) and allow other routers to make decisions based on that tag.
Any BGP router can tag routes in incoming and outgoing routing updates, or when doing redistribution.
Any BGP router can filter routes in incoming or outgoing updates or can select preferred routes based on communities (the tag).
Communities are not restricted to one network or one autonomous system, and they have no physical boundaries.
Communities are optional transitive attributes.

## Slide 97: The MED Attribute
The MED attribute, also called the metric , is an optional nontransitive attribute.
The MED indicates to external neighbors the preferred path into an autonomous system. This is a dynamic way for an autonomous system to try to influence another autonomous system as to which way it should choose to reach a certain route if there are multiple entry points into the autonomous system.
A lower metric value is preferred.
Unlike local preference, the MED is exchanged between autonomous systems. The MED is sent to eBGP peers; those routers propagate the MED within their autonomous system, and the routers within the autonomous system use the MED, but do not pass it on to the next autonomous system.
When the same update is passed on to another autonomous system, the metric will be set back to the default of 0.
Notes: By default, a router compares the MED attribute only for paths from neighbors in the same autonomous system.
By using the MED attribute, BGP is the only protocol that can try to affect the path used to send traffic into an autonomous system. However, keep in mind that there is no guarantee that neighboring autonomous system will take the MED attribute into account; it may have already decided on the path based on other attributes.

## Slide 98: MED Example

## Slide 99: The Weight Attribute (Cisco Only)
The weight attribute is a Cisco-defined attribute used for the path-selection process.
The weight attribute is configured locally and provides local routing policy only; it is not propagated to any BGP neighbors.
Routes with a higher weight are preferred when multiple routes to the same destination exist.
The weight can have a value from 0 to 65535. Paths that the router originates have a weight of 32768 by default, and other paths have a weight of 0 by default.

## Slide 100: The Weight Attribute (Cisco Only)

## Slide 101: Changing the Weight Using Route Maps

## Slide 102: Influencing BGP Path Selection

## Slide 103: show ip bgp

## Slide 104: show ip route bgp

## Slide 105: traceroute

## Slide 106: ISP3
Notes: Highest Uptime route is chosen

## Slide 107: Changing the Weight
Notes: Routes with a higher weight are preferred when multiple routes to the same destination exist.

## Slide 108: Changing the Weight

## Slide 109: Changing Local Preference

## Slide 110: Changing Local Preference

## Slide 111: Setting the AS-Path
It is complicated to influence other autonomous systems to select a particular path for traffic that is returning to a specific autonomous system
One way that an autonomous system can attempt to influence incoming traffic flow is by sending out eBGP updates with an extended AS-path attribute for undesired paths
Notes: To avoid clashes with BGP loop-prevention mechanisms, no other autonomous system number, except that of the sending autonomous system, should be prepended to the AS-path attribute. If another autonomous system number is prepended in the autonomous system path, the routers in the autonomous system that has been prepended will reject the update because of BGP loop-prevention mechanisms.

## Slide 112: Setting the AS-Path

## Slide 113: Setting the AS-Path

## Slide 114
Controlling BGP Routing Updates

## Slide 115: Controlling BGP Routing Updates
If there are multiple paths between your network and ISP, you may need to filter certain information during the exchange of BGP updates to influence the route selection or to enforce an administrative policy.
BGP peer groups are used to group peers with similar policies together for a simpler, more efficient configuration.

## Slide 116: Filtering BGP Routing Updates
BGP Filtering Using Prefix Lists
BGP Filtering Using AS-Path Access Lists
BGP Filtering Using Route Maps
Filtering Order

## Slide 117: BGP Filtering Using Prefix Lists
The neighbor ip-address prefix-list prefix-list-name { in | out } router configuration command is used to apply a prefix list to routes from or to a neighbor.

## Slide 118: BGP Filtering Using Prefix Lists - Example
Notes: For example, consider Figure 7-19 and the configuration on router R2 in Example 7-43 .
The prefix list named ANY-8to24-NET is configured to match routes from any networks that have a mask length from 8 to 24 bits.
The 0.0.0.0/0 network/length combination does not match a specific network; rather, it defines any network. The parameters ge 8 and le 24 specify that any network with the mask length between 8 and 24 matches the prefix list entry.

## Slide 119: BGP Filtering Using AS-Path Access Lists
The autonomous system path access list is defined by the ip as-path access-list accesslist-number { permit | deny } regexp global configuration command

## Slide 120: BGP Filtering Using AS-Path Access Lists
The neighbor ip-address filter-list access-list-number { in | out } router configuration command is used to apply an AS-path access list to routes from or to a neighbor.

## Slide 121: BGP Filtering Using AS-Path Access Lists - Example
Notes: Consider the multihomed ISP customer in Figure 7-20 . Autonomous system 65000 does not want to act as a transit autonomous system between its service providers.
This situation is avoided by ensuring that only locally sourced routes are sent to the ISP, and then the customer avoids receiving IP packets from the ISPs for destinations outside its own autonomous system.
The configuration for the GW1 and GW2 routers is shown in Example 7-44 . The AS-path access list permits only the empty string, matched by the regular expression ^$ , which represents locally sourced routes.
By applying this filter list on outgoing information to all neighbors, the customer announces only its local routes.

## Slide 122: BGP Filtering Using Route Maps
A route map can match and set several different BGP attributes, including the following:
  Origin
  Next hop
  Community
  Local preference
  MED
Route maps can match based on other items, including the following:
  Network number and subnet mask (with an IP prefix list)
  Route originator
  Tag an IGP route
  AS-path
  Route type (internal or external)

## Slide 123: BGP Filtering Using Route Maps

## Slide 124: BGP Peer Groups
In BGP, many neighbors are often configured with the same update policies.
On a Cisco IOS router, neighbors with the same update policies can be grouped into peer groups to simplify configuration and, more important, to make updating more efficient and improve performance.
A peer group’s configuration can have many BGP features, including the following:
  update-source
  next-hop-self
  ebgp-multihop
  Authentication of the BGP sessions
  Change the weight of routes received
  Filter incoming or outgoing routes

## Slide 125: Peer Group Configuration
The neighbor peer-group-name peer-group router configuration command is used to create a BGP peer group.
The neighbor ip-address peer-group peer-group-name router configuration command, is used to assign neighbors as part of the group after the group has been created.
Notes: The clear ip bgp peer-group peer-group-name EXEC command is used to reset the BGP connections for all members of a BGP peer group. The peer-group-name is the name of the BGP peer group for which connections are to be cleared.

## Slide 126: Peer Group Configuration Example

## Slide 127: Peer Group Configuration Example

## Slide 128: Implementing BGP for IPv6 Internet Connectivity

## Slide 129: Implementing BGP for IPv6 Internet Connectivity
This section covers the following topics:
MP-BGP support for IPv6
Exchanging IPv6 routes over an IPv4 session
Exchanging IPv6 routes over an IPv6 session
BGP for IPv6 configuration and verification
Comparing IPv4 to Dual (IPv4/IPv6) BGP transport
BGP filtering mechanisms for IPv6
Notes: MP-BGP is capable of carrying a rich set of routed protocols, including IPv4 and IPv6, over a transport protocol, such as IPv4 or IPv6.

## Slide 130: MP-BGP Support for IPv6
Multiprotocol extensions are defined as new attributes. IPv6-specific extensions incorporated into MBGP include the following:
A new identifier for the IPv6 address family.
Scoped addresses. The next-hop attribute contains a global IPv6 address or a link-local address.
The next-hop attribute and NLRI are expressed as IPv6 addresses and prefixes
Notes: When link-local addresses are used for peering with a neighbor BGP router, these link-local IPv6 addresses are used as the next-hop addresses for the routes that are carried by BGP.
In some cases, the next-hop IPv6 addresses need to be changed to a global IPv6 address, using a route map in the neighbor configuration statement.
. (Recall that the NLRI field in a BGP update message lists the networks reachable on the BGP path described by the update message.)

## Slide 131: MP-BGP
MP-BGP can, of course, operate with multiple protocols. It operates by identifying two separate protocols: the carrier protocol and the passenger protocol.
In an all-IPv4 environment, BGP establishes sessions using IPv4 (using TCP port 179); IPv4 is the carrier protocol.
The routes that BGP advertises, which is the passenger protocol, are also IPv4.

## Slide 132: MP-BGP
Protocols other than IPv4, including IPv6, also need to advertise reachability information.
MP-BGP extensions allow these other protocols to be carried using BGP.

## Slide 133: MP-BGP
In an all-IPv6 environment, BGP can be used as both the carrier and passenger protocol.
In this case, IPv6 is used to establish BGP sessions, and BGP advertises IPv6 prefixes.

## Slide 134: Exchanging IPv6 Routes over an IPv4 Session
Existing IPv4 TCP sessions can carry IPv6 routing information when adding IPv6 support to a network.
An existing neighbor can be activated for the IPv6 address family and IPv6 routing information will be sent over the same neighbor session.
MP-BGP allows the use of many address families to define the type of addresses being carried.
Notes: The most common address families are IPv4, IPv6, and VPNv4 and VPNv6 (for MPLS VPN routes). This chapter discusses only the IPv4 and IPv6 address families

## Slide 135: Exchanging IPv6 Routes over an IPv4 Session
The address-family {ipv4 | ipv6} [ unicast | multicast ] router configuration command enters address family configuration mode for configuring BGP routing sessions.

## Slide 136: Exchanging IPv6 Routes over an IPv4 Session
In an IPv6 address family, a neighbor needs to be activated using the neighbor { IPv4 address | IPv6 address } activate address-family configuration command.
The exchange of addresses with BGP neighbors is enabled for the IPv4 address family by default.
The network ipv6-address/prefix-length command, this time in address family configuration mode, is used to specify the networks to be advertised.
This command injects a prefix into the BGP database only for the specified address family

## Slide 137: Exchanging IPv6 Routes over an IPv4 Session

## Slide 138: Exchanging IPv6 Routes over an IPv6 Session
Notes: Of course, MP-BGP also supports exchanging IPv6 routes over an IPv6 session.
By default, BGP sets its router ID to the IPv4 address of the highest address of the loopback interface, or if no loopback exists, to the highest IP address of the physical interface.
If a router running BGP over IPv6 transport has no IPv4 addresses configured, you need to manually specify BGP router ID. The bgp router-id ip-address router configuration command configures a fixed router ID for the local BGP routing process; this command is required in an IPv6-only network. The ip-address parameter is an IPv4-address format 32-bit dotted-decimal number.

## Slide 139: BGP for IPv6 Configuration and Verification

## Slide 140: BGP for IPv6 Configuration and Verification

## Slide 141: BGP for IPv6 Configuration and Verification

## Slide 142: BGP for IPv6 Configuration and Verification

## Slide 143: BGP for IPv6 Configuration and Verification

## Slide 144: BGP for IPv6 Configuration and Verification

## Slide 145: BGP for IPv6 Configuration and Verification

## Slide 146: BGP for IPv6 Configuration and Verification

## Slide 147: Enable eBGP IPv6 Route Exchange

## Slide 148: Enable eBGP IPv6 Route Exchange

## Slide 149: Enable eBGP IPv6 Route Exchange

## Slide 150: Enable eBGP IPv6 Route Exchange

## Slide 151: Enable eBGP IPv6 Route Exchange
The eBGP IPv6 update received on R1 is not marked as best (using the > sign) in the BGP table, because the next-hop address is not reachable.
Also the next-hop address, ::FFFF:172.16.12.2, is an IPv6 address derived from the IPv4 next-hop address.
This neighbor relationship is an IPv4 neighbor relationship, carrying IPv6 routes.
Because an IPv6 route must have an IPv6 next hop, BGP dynamically created this IPv6 next-hop address from the actual IPv4 next-hop address.
However, this is not a reachable IPv6 address; therefore, the route is not marked as best in the BGP table, and it does not appear in the IPv6 routing table.

## Slide 152: Enable eBGP IPv6 Route Exchange

## Slide 153: Enable iBGP IPv6 Route Exchange

## Slide 154: Enable iBGP IPv6 Route Exchange

## Slide 155: Enable iBGP IPv6 Route Exchange

## Slide 156: Comparing IPv4 to Dual (IPv4/IPv6) BGP Transport
As you have seen, both IPv4 and IPv6 address families can use a single IPv4 neighbor or two separate sessions can be established, one for each address family.
There are advantages to both approaches.
Using a single IPv4 neighbor reduces the number of neighbor sessions. In an environment where a lot of neighbors are configured, this can significantly reduce the size and complexity of configuration.
However, running IPv6 over an IPv4 session requires modification of the next-hop attribute.
In contrast, when using two separate sessions for IPv4 and IPv6, there is no need to implement route maps to overwrite the next-hop parameter.
Exchange of IPv4 and IPv6 routes is completely independent; neighbor configuration and handling is duplicated.
Note that IPv6 neighbors are not seen in the show ip bgp summary command output; use the show bgp ipv6 unicast summary command instead.

## Slide 157: BGP Filtering Mechanisms for IPv6
IPv6 Prefix List Filtering
IPv6 Path Selection with BGP Local Preference

## Slide 158: IPv6 Prefix List Filtering

## Slide 159: IPv6 Path Selection with BGP Local Preference

## Slide 160
Appendix C

## Slide 161: BGP Supplement
BGP Route Summarization
Communities
Route Reflectors
Advertising a Default Route
Not Advertising Private Autonomous System Numbers

## Slide 162: BGP Route Summarization
Two BGP attributes are related to aggregate addressing:
Atomic aggregate
  A well-known discretionary attribute that informs the neighbor autonomous system that the originating router has aggregated the routes
Aggregator
  An optional transitive attribute that specifies the BGP router ID and autonomous system number of the router that performed the route aggregation

## Slide 163: BGP Route Summarization
By default, the aggregate route is advertised as coming from the autonomous system that did the aggregation and has the atomic aggregate attribute set to show that information might be missing.
The autonomous system numbers from the nonaggregated routes are not listed.
You can configure the router to include the unordered list of all autonomous systems contained in all paths that are being summarized.

## Slide 164: Network Boundary Summarization
BGP works differently than the other protocols, the network network-number [ mask network-mask ] router configuration command for BGP permits BGP to advertise a network if it is present in the IP routing table.
This command allows classless prefixes. The router can advertise individual subnets, networks, or supernets. The default mask is the classful mask and results in only the classful network number being announced.
Note that at least one subnet of the specified major network must be present in the IP routing table for BGP to start announcing the classful network. However, if you specify the mask network-mask , an exact match to the network (both address and mask) must exist in the routing table for the network to be advertised.
Notes: Consider how other protocols handle summarization. The Routing Information Protocol Version 1 (RIPv1) and Routing Information Protocol Version 2 (RIPv2) protocols summarize routes on the classful network boundary by default

## Slide 165: Network Boundary Summarization
The BGP auto-summary command determines how BGP handles redistributed routes.
The no auto-summary router configuration command turns off BGP autosummarization.
When summarization is enabled (with auto-summary ), all redistributed subnets are summarized to their classful boundaries in the BGP table.
When summarization is disabled (with no auto-summary ), all redistributed subnets are present in their original form in the BGP table.

## Slide 166: BGP Route Summarization Using the network Command
To advertise a simple classful network number, use the network network-number router configuration command without the mask option.
To advertise an aggregate of prefixes that originate in this autonomous system, use the network network-number [ mask network-mask ] router configuration command with the mask option.
Remember that the prefix must exactly match [both address and mask] an entry in the IP routing table for the network to be advertised
Notes: For BGP, the network command requires that there be an exact match in the routing table for the prefix or mask that is specified. This exact match can be accomplished by using a static route with a null 0 interface, or it might already exist in the routing table, such as because of the Interior Gateway Protocol (IGP) performing the summarization.

## Slide 167: Cautions When Using the network Command for Summarization

## Slide 168: Cautions When Using the network Command for Summarization
Each of the four Class C networks is announced because each already exists in the routing table. These networks are summarized with the network 192.168.24.0 mask 255.255.252.0 command on Router C.
However, with this command the 192.168.24.0/22 route is not announced by default because that route is not in the routing table
Correct way for summarization with the network command:

## Slide 169: Creating a Summary Address in the BGP Table Using the aggregate-address Command
The aggregate-address ip-address mask [ summary-only ] [ as-set ] router configuration command is used to create an aggregate, or summary, entry in the BGP table.

## Slide 170: Compare…
Notice the difference between the aggregate-address and the network command:
The aggregate-address command aggregates only networks that are already in the BGP table .
With the BGP network command, the network must exist in the IP routing table for the summary network to be advertised.
Notes: When you use the aggregate-address command without the as-set keyword, the aggregate route is advertised as coming from your autonomous system, and the atomic aggregate attribute is set to show that information might be missing. The atomic aggregate attribute is set unless you specify the as-set keyword.

## Slide 171: Using the aggregate-address Command
When you use the aggregate-address command without the as-set keyword, the aggregate route is advertised as coming from your autonomous system, and the atomic aggregate attribute is set to show that information might be missing. The atomic aggregate attribute is set unless you specify the as-set keyword.
Without the summary-only keyword, the router still advertises the individual networks.
When the aggregate-address command is used, a BGP route to null 0 is automatically installed in the IP routing table for the summarized route.
For BGP to announce a summary route using the aggregate-address command, at least one of the more specific routes must be in the BGP table.

## Slide 172: aggregate-address Example

## Slide 173: aggregate-address Example
Notes: The show ip bgp command provides information about route summarization and displays the local router ID, the networks recognized by the BGP process, the accessibility to remote networks, and autonomous system path information. In Example C-4 , notice the s in the first column for the lower four networks. These networks are being suppressed. They were learned from a network command on this router. The next-hop address is 0.0.0.0, which indicates that this router created these entries in BGP. Notice that this router also created the summarized route 192.168.24.0/22 in BGP (this route also has a next hop of 0.0.0.0, indicating that this router created it). The more-specific routes are suppressed, and only the summarized route is announced.

## Slide 174: Communities
The BGP communities function allows routers to tag routes with an indicator (the community) and allows other routers to make decisions (filter) based on that tag.
BGP communities are used for destinations (routes) that share some common properties and that, therefore, share common policies.
Routers, therefore, act on the community, rather than on individual routes.
Communities are not restricted to one network or autonomous system, and they have no physical boundaries.

## Slide 175: Community Attribute
The community attribute is an optional transitive attribute. If a router does not understand the concept of communities, it passes it on to the next router. However, if the router does understand the concept, it must be configured to propagate the community. Otherwise, communities are dropped by default.
Each network can be a member of more than one community.
The community attribute is a 32-bit number.
The upper 16 bits indicate the autonomous system number of the autonomous system that defined the community.
The lower 16 bits are the community number and have local significance.

## Slide 176: Setting the Communities Configuration
Route maps can be used to set the community attributes.
The set community {[ community-number ] [ well-known-community ] [ additive ]} | none route map configuration command is used within a route map to set the BGP community attribute.
Notes: Or community number or well-known-community

## Slide 177: Sending the Communities Configuration
The set community command is used along with the neighbor route-map command to apply the route map to updates.
The neighbor { ip-address | peer-group-name } send-community router configuration command is used to specify that the BGP communities attribute should be sent to a BGP neighbor.
By default, the communities attribute is not sent to any neighbor. (Communities are stripped in outgoing BGP updates.)

## Slide 178: BGP Communities Example
Notes: In this example, Router C has one neighbor, 10.10.20.1 (Router A). When communicating with Router A, the community attribute is sent, as specified by the neighbor send-community command. The route map SETCOMM is used when sending routes to Router A to set the community attribute. Any route that matches access-list 1 has the community attribute set to no-export . Access list 1 permits any routes.
Therefore, all routes have the community attribute set to no-export.
In this example, Router A receives all of Router C’s routes but does not pass them to Router B.

## Slide 179: Using the Communities Configuration
The ip community-list community-list-number { permit | deny } community-number global configuration command is used to create a community list for BGP and to control access to it.

## Slide 180: Using the Communities Configuration
The match community community-list-number [ exact ] route map configuration command enables you to match a BGP community attribute to a value in a community list.

## Slide 181: BGP Communities Example Using Weight

## Slide 182: BGP Communities Example Using Weight
Notes: In this example, Router A has a neighbor, 10.10.20.2 (Router C). The route map CHKCOMM is used when receiving routes from Router C to check the community attribute. Any route whose community attribute matches community list 1 has its weight attribute set to 20. Community list 1 permits routes with a community attribute of 100.
Therefore, all routes from Router C (which all have 100 in their list of communities) have their weight set to 20.
In this example, any route that does not match community list 1 is checked against community list 2. Any route matching community list 2 is permitted but does not have any of its attributes changed. Community list 2 specifies the internet keyword, which means all routes.

## Slide 183: BGP Communities Example Using Weight

## Slide 184: Route Reflectors
BGP specifies that routes learned via iBGP are never propagated to other iBGP peers.
The result is that a full mesh of iBGP peers is required within an autonomous system.
With only 13 routers, 78 iBGP sessions would need to be maintained.
As the number of routers increases, so does the number of sessions required, governed by the following formula, in which n is the number of routers:
Number of iBGP sessions = n ( n – 1) / 2

## Slide 185: Route Reflectors (PANIC MODE )

## Slide 186: Route Reflectors
In addition to the number of BGP TCP sessions that must be created and maintained, the amount of routing traffic might also be a problem.
Depending on the autonomous system topology, traffic might be replicated many times on some links as it travels to each iBGP peer.
For example, if the physical topology of a large autonomous system includes some WAN links, the iBGP sessions running over those links might consume a significant amount of bandwidth.
A solution to this problem is the use of route reflectors (RRs).
This section describes what an RR is, how it works, and how to configure it.
RRs modify the BGP rule by allowing the router configured as the RR to propagate routes learned by iBGP to other iBGP peers

## Slide 187: Route Reflectors
This saves on the number of BGP TCP sessions that must be maintained and also reduces the BGP routing traffic.

## Slide 188: Route Reflector Benefits
With a BGP RR configured, a full mesh of iBGP peers is no longer required.
The RR is allowed to propagate iBGP routes to other iBGP peers.
Route reflectors reduce the number of BGP neighbor relationships in an autonomous system by having key routers replicate updates to their RR clients.
Route reflectors do not affect the paths that IP packets follow.
Only the path that routing information is distributed on is affected.
An autonomous system can have multiple RRs, both for redundancy and for grouping to further reduce the number of iBGP sessions required.
Migrating to RRs involves a minimal configuration and does not have to be done all at one time, because routers that are not RRs can coexist with RRs within an autonomous system.
Notes: RRs are used mainly by ISPs when the number of internal neighbor statements becomes excessive.
However, if RRs are configured incorrectly, routing loops might result, as shown in the example later in this appendix in the “Route Reflector Migration Tips” section.

## Slide 189: Route Reflector Terminology
Route Reflector:
  Router that is configured to be the router allowed to advertise (or reflect) routes it learned via iBGP to other iBGP peers.
Clients:
  Routers peering with the RR has a partial iBGP
  Peering between the clients is not needed, because the route reflector passes advertisements between the clients.
Cluster:
  The combination of the RR and its clients
Nonclients:
  Other iBGP peers of the RR that are not clients
Originator ID:
  Is an optional, nontransitive BGP attribute that is created by the RR.
  This attribute carries the router ID of the route’s originator in the local autonomous system.
  If the update comes back to the originator because of poor configuration, the originator ignores it.

## Slide 190: Route Reflector Terminology
Cluster ID :
  Usually a cluster has a single RR, in which case the cluster is identified by the RR’s router ID.
  To increase redundancy and avoid single points of failure, a cluster might have more than one RR. When this occurs, all the RRs in the cluster need to be configured with a Cluster ID.
  The cluster ID allows route reflectors to recognize updates from other RRs in the same cluster.
Cluster list
  Is a sequence of cluster IDs that the route has passed. When an RR reflects a route from its clients to nonclients outside the cluster, it appends the local cluster ID to the cluster list. If the update has an empty cluster list, the RR creates one.
  Using this attribute, an RR can tell whether the routing information is looped back to the same cluster because of poor configuration.
  If the local cluster ID is found in an advertisement’s cluster list, the advertisement is ignored.
  The originator ID, cluster ID, and cluster list help prevent routing loops in RR configurations.

## Slide 191: Route Reflector Design
When using RRs in an autonomous system, you can divide the autonomous system into multiple clusters, each having at least one RR and a few clients. Multiple RRs can exist in one cluster for redundancy.
The RRs must be fully meshed with iBGP to ensure that all routes learned are propagated throughout the autonomous system.
An IGP is still used, just as it was before RRs were introduced, to carry local routes and next-hop addresses.
Normal split-horizon rules still apply between an RR and its clients. Thus an RR that receives a route from a client does not advertise that route back to that client.

## Slide 192: Route Reflector Design Example
Notes: Routers B, D, E, and F form one cluster. Routers C, G, and H form another cluster. Routers B and C are RRs. Routers A, B, and C are fully meshed with iBGP.
Note that the routers within a cluster are not fully meshed.

## Slide 193: Route Reflector Operation
When an RR receives an update, it takes the following actions, depending on the type of peer that sent the update:
If the update is from a client peer, it sends the update to all nonclient peers and to all client peers (except the route’s originator).
If the update is from a nonclient peer, it sends the update to all clients in the cluster.
If the update is from an eBGP peer, it sends the update to all nonclient peers and to all client peers.

## Slide 194: Route Reflector Migration Tips
When migrating to using RRs, the first consideration is which routers should be the reflectors and which should be the clients.
Following the physical topology in this design decision ensures that the packet-forwarding paths are not affected.
Not following the physical topology (for example, configuring RR clients that are not physically connected to the route reflector) might result in routing loops.

## Slide 195: Bad Route Reflector Design
Notes: Bad Route Reflector Design That Does Not Follow the Physical Topology

## Slide 196: Bad Route Reflector Design
In this bad design , which does not follow the physical topology, the following happens:
Router B knows that the next hop to get to 10.0.0.0 is x (because it learns this from its RR, Router C).
Router A knows that the next hop to get to 10.0.0.0 is y (because it learns this from its RR, Router D).
For Router B to get to x , the best route might be through Router A, so Router B sends a packet destined for 10.0.0.0 to Router A.
For Router A to get to y , the best route might be through Router B, so Router A sends a packet destined for 10.0.0.0 to Router B.
This is a routing loop.

## Slide 197: Good Route Reflector Design

## Slide 198: Good Route Reflector Design
In this good design , which follows the physical topology, the following are true:
Router B knows that the next hop to get to 10.0.0.0 is y (because it learns this from its RR, Router D).
Router A knows that the next hop to get to 10.0.0.0 is x (because it learns this from its RR, Router C).
For Router A to get to x , the best route is through Router C, so Router A sends a packet destined for 10.0.0.0 to Router C, and Router C sends it to Router E.
For Router B to get to y , the best route is through Router D, so Router B sends a packet destined for 10.0.0.0 to Router D, and Router D sends it to Router E.
There is no routing loop.

## Slide 199: Route Reflector Configuration

## Slide 200: Advertising a Default Route
The neighbor { ip-address | peer-group-name } default-originate [ route-map map-name ] router configuration command can be used for a BGP router to send the default route 0.0.0.0 to a neighbor, for its use as a default route.

## Slide 201: Not Advertising Private Autonomous System Numbers
IANA defines private autonomous system numbers 64512 through 65534 to be used for private purposes.
Only public autonomous system numbers should be sent to eBGP neighbors on the Internet.

## Slide 202: Not Advertising Private Autonomous System Numbers
Use the neighbor { ip-address | peer-group-name } remove-private-as [ all [ replace-as ]] router configuration command to remove private autonomous system numbers from the AS-Path attribute; this command is available only for eBGP neighbors

## Slide 203: Chapter 7 Summary
BGP terminology and concepts, including the following:
BGP’s use between autonomous systems and how it is different than other routing protocols described in this book
BGP’s classification as a path vector protocol and its use of TCP protocol 179
BGP’s loop-free guarantee, because it does not accept a routing update that already includes its autonomous system number in the AS-path list
The three tables used by BGP: the BGP table, IP routing table, and BGP neighbor table
The four BGP message types: open, keepalive, update, and notification
When to use BGP: if the autonomous system allows packets to transit through it to reach other autonomous systems, if the autonomous system has multiple connections to other autonomous systems, or if the routing policy and route selection for traffic entering and leaving the autonomous system must be manipulated
The use of full-mesh iBGP on all routers in the transit path within the autonomous system

## Slide 204: Chapter 7 Summary
When not to use BGP: if there is only a single connection to the Internet or another autonomous system, if edge routers have a lack of memory or processing power, if you have a limited understanding of route filtering and the BGP path-selection process, or if the routing policy that will be implemented in an autonomous system is consistent with the policy implemented in the ISP autonomous system
BGP neighbor (peer) relationships:
iBGP, when BGP runs between routers in the same autonomous system
eBGP, when BGP runs between routers that are in different autonomous systems.
eBGP neighbors are typically directly connected .

## Slide 205: Chapter 7 Summary
Basic BGP configuration, including the relationship between the BGP table, the IP routing table and the network command: The network command allows a BGP router to inject a network that is in its IP routing table into its BGP table and advertise that network to its BGP neighbors. BGP neighbors exchange their best BGP routes.
The neighbor router that receives that network information puts the information in its BGP table and selects its best BGP route for that network. The best route is offered to its IP routing table.
Using BGP features, including next-hop-self, update source, and eBGP multihop.
Understanding and troubleshooting the BGP states: idle, connect, active, open sent, open confirm, and established.
Performing hard and soft resets of BGP sessions, required after a neighbor policy is changed.

## Slide 206: Chapter 7 Summary
The BGP attributes that can be either well-known or optional, mandatory or discretionary, and transitive or nontransitive. An attribute might also be partial. The BGP attributes are the following:
  AS-path: Well-known mandatory. The list of autonomous system numbers that a route has traversed to reach a destination, with the number of the autonomous system that originated the route at the end of the list.
  Next hop: Well-known mandatory. Indicates the next-hop IP address that is to be used to reach a destination. For eBGP, the next hop is the IP address of the neighbor that sent the update; for iBGP, the next hop advertised by eBGP is carried into iBGP by default.
  Origin: Well-known mandatory. Defines the origin of the path information; can be IGP, EGP, or incomplete.
  Local preference: Well-known discretionary. Indicates to routers in the autonomous system which path is preferred to exit the autonomous system. The path with a higher local preference is preferred. Sent only to iBGP neighbors.
  Atomic aggregate: Well-known discretionary. Informs the neighbor autonomous system that the originating router has aggregated the routes.

## Slide 207: Chapter 7 Summary
  Aggregator: Optional transitive. Specifies the BGP router ID and autonomous system number of the router that performed the route aggregation.
  Community: Optional transitive. Allows routers to tag routes with an indicator (the community) and allows other routers to make decisions based on that tag.
  MED: Optional nontransitive. Also called metric. Indicates to external neighbors the preferred path into an autonomous system. A lower value is preferred; exchanged between autonomous systems.
  Weight: Cisco defined; provides local routing policy only and is not propagated to any BGP neighbors. Routes with a higher weight are preferred.

## Slide 208: Chapter 7 Summary
The 11-step BGP route-selection decision process is as follows:
  1. Prefer the highest weight.
  2. Prefer the highest local preference.
  3. Prefer the route originated by the local router.
  4. Prefer the shortest AS-path.
  5. Prefer the lowest origin code.
  6. Prefer the lowest MED.
  7. Prefer the eBGP path over the iBGP path.
  8. Prefer the path through the closest IGP neighbor.
  9. Prefer the oldest route for eBGP paths.
  10. Prefer the path with the lowest neighbor BGP router ID.
  11. Prefer the route with the lowest neighbor IP address.

## Slide 209: Chapter 7 Summary
Verifying BGP configuration.
BGP path manipulation and filtering, including changing the weight, local preference, AS-path, and MED attributes. Prefix lists, distribute lists, filter lists, and route maps may be used.
Configuring BGP peer groups, a group of BGP neighbors of the router being configured that all have the same update policies.
Implementing MP-BGP for IPv6, including the following:
Exchanging IPv6 routes over an IPv4 session
Exchanging IPv6 routes over an IPv6 session
BGP filtering mechanisms used for IPv6.

## Slide 210: Chapter 7 Labs
CCNPv7 ROUTE Lab7.1 BGP Config
CCNPv7 ROUTE Lab7.2 BGP AS PATH
CCNPv7 ROUTE Lab7.3 IBGP EBGP LocalPref MED
CCNPv7 ROUTE Lab7.4 IBGP EBGP Synchronization
CCNPv7 ROUTE Lab7.5 MP-BGP

## Slide 212: Acknowledgment
Some of images and texts are from Implementing Cisco IP Routing (ROUTE) Foundation Learning Guide by Diane Teare, Bob Vachon and Rick Graziani (1587204568)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva